## Slide 1: Digital Data Communications in Air Quality Monitoring
Better, cheaper, faster?
Erik Aaboe, New Mexico Environment Department

## Slide 2: Questions?
How many are familiar with their monitoring system communications methods?
Who knows what they cost?
  Everyone satisfied with that cost?
Who uses Leased Lines?
Part of a Local Area Network?
Plain Old Telephone Services?
Analog Cellular?
Digital Cellular?
Digital Subscriber Lines / Cable Internet?

## Slide 3: NMED Situation
23 continuous monitoring sites
All on Plain Old Telephone Services (POTS) lines
Worked fine for daily polling
Hourly calls costly
  (for real-time web & AIRNow posting)
Short-term solutions
  Reduce call frequency (every other hour, etc.)
  Split polling assignments to LAN locations with local calls
  Change analog cellular to local phone number

## Slide 4: NMED Phone Costs & Issues
~$42.00 / month for phone service at each site
Long distance charges for hourly calls at 8760 hours / year.
Each call at approximately one minute = $876 for total cost of ~$1350 / site / year
Phone lines not at all desired locations

## Slide 5: Digital Cellular
Device $350-$550 to connect each site to Internet
Poll from polling machine over Internet
Data Plan for service – depends upon usage
  2 MB / month = $10 / month
No per-call connection costs
If desired, can download shorter interval data (5 minute & 15 minute averages, e.g.)

## Slide 6: Digital Modem Technologies Available
Airlink Redwing
  “unintelligent” device acts as modem for PC-based systems
  Establishes DUN (dial-up networking) connection to Internet
  Setup with a static IP address
Airlink Raven
  Same capabilities but has embedded Operating System for traditional datalogger systems

## Slide 8
Raven
Features
High speed data transfer rate
Full duplex transceiver
Low power consumption
iDEN - Nextel
CDMA 1XRTT – VZW, SPCS, Alltel
GPRS, EDGE – Cingular, Dobson
Environmental operating range –30 to +75 C
LEDs show status of modem operation
Serial port for mobile data applications
Over the air programmable firmware upgrades
On-board ARM processor - ALEOS
Class I Division II certified (Gas & Oil Industry)
Applications
Utilities
Telemetry/SCADA
Fire/EMS/Police
Workforce Automation
ATM/POS
Router Back-up

## Slide 9
SCADA, Telemetry, and Data Acquisition

## Slide 10
<footer>
<date/time>
Verizon “Enhanced” Coverage Map

## Slide 11: Possible Digital Cellular Issues
Can my polling system connect to an IP address?
Does device work with my datalogging system?
Does the remote system stay connected?
  One line batch file to reconnect for PCs with Redwings
  Stayalive ping feature for Ravens
Will my IT department allow this technology?
Does it save money or improve performance?
Is the remote equipment secure?

## Slide 12: Security
Securing Remote Devices
  IPSec for PC based systems (on W2000, XP PCs)
  “Friendly IP” list for Raven
  Only acknowledge approved IP addresses or subnets
  Invisible to the rest of the Internet
Getting Through Agency Firewalls
  Port usage for polling (use 443 or 8088 or a commonly open port)
  To set rules on remote system – are agency IP addresses NATted? Go to http://whatismyip.com or http://dnsstuff.com from polling PC to determine

## Slide 13: Possible Benefits
More bandwidth available than current system?
Connect to remote system using remote access tools without interrupting polling
Allow connections from others (support contractors, troubleshooters, site operators from home, etc.)
Poll data from multiple locations?

## Slide 14: Thank You
For information contact erik.aaboe@state.nm.us
Questions?