## Slide 1: SAUNA The Sodankyla validation campaign
Richard McPeters and Bojan Bojkov
NASA/GSFC
University of Maryland
Aura Science Team, Pasadena CA October 1, 2007

## Slide 2: Total column ozone issues
Currently:
  Satellite measurements agree within 2-3% globally
  Differences at low sun, high column amounts, high reflectivities, etc.
Need to verify the accuracy of ground-based measurements for satellite validation purposes

## Slide 3: Total column ozone issues (2)
In an attempt to better understand the column issues, NASA, ESA and FMI conducted two field campaigns
  Focus during high column, low sun periods in Northern Finland
    SAUNA: March-April 2006
    SAUNA 2: February-April 2007
  Combined network instruments: Dobsons, Brewers, DOAS, sondes and LIDAR
  Included World and European standard instruments
  Involved more than 30 Scientists from 12 institutes in 10 countries

## Slide 4
Ozone measurements made by double Brewer throughout the day on April 5, 2006. The double Brewer is assumed to be accurate for SZA < 80°

## Slide 5
Dobson measurements made with AD pair to ~65° SZA, the switch to CD pair.

## Slide 6
OMI agreed well with ground based measurements during two overpasses. Single Brewer shows some error at high SZA (high slant column ozone).

## Slide 9: SAUNA (column) summary
SAUNA behavior seen at other high and mid-latitude sites
Data from double Brewers should be used for Aura ozone validation at high solar zenith angles
The state of the network calibration (Brewer and Dobson) are uncertain and may require improvements
With improved GB calibration, differences most probably due to ozone X-sections uncertainties
  High spectral resolved X-section required which can be used by both satellites and ground-based instruments