## Slide 1: GPS Re-radiators
Army Spectrum Management Office
Stevan Jovancevic
Date: October 28, 2005

## Slide 2: GPS Re-radiators
Purpose: To examine use of GPS Re-radiators for military applications.
GPS Re-radiators receive the GPS signal and retransmit it to users who otherwise could not be able to get a lock on the GPS signal due to superstructure blockage.
IRAC has generated regulations for the use of these devices by the Government agencies which includes the military.
Military has unique requirements for utilization of the GPS Re-radiating kits.

## Slide 3: Present Army Operations in IRAQ

## Slide 4: Army Applications of the GPS Re-radiators
Army troops are engaged in the present day conflict in IRAQ.
Position Location is necessary for successful mission execution.
Troops are being transported in the armored vehicles such as Bradley Fighting Vehicle and Stryker Brigade Combat Vehicles.
Special Operations Forces utilization in transport vehicles and cargo planes (C-130).
Feedback from users includes a request for utilization aboard the fixed wing and rotary wing aircraft.
A significant number of Humvees are also armor plated.

## Slide 5: Reception of the GPS Signal
GPS Signal is unable to propagate inside armored vehicles.
Our troops are unable to receive the GPS signal inside Bradley Combat Vehicles, Humvees, or Stryker Brigade Combat Vehicles.
Solution: Use the GPS Re-radiator to obtain a GPS signal. Troops can tolerate certain GPS signal error.

## Slide 6: Feedback from the troops
Mr. Ryberg,
believe me, this is one of the BEST products I have ever seen for a military application!!!!
I bought one for myself about 2 years ago and used the HE** out of it!!! it was the ONLY thing on earth that allowed GPS's (garmin's and PSN-11 and other GPS's) to work inside the vehicle (armored and non armored).
I went to Iraq without one (in april 2004) and drove around with my hand out the window of a armored humvee... doesnt seem like that makes much sense, but in order to know where I was going, I had to have line of sight. Now since Nov 2004 (when i purchased mine) with the VORTECH reradiator, I can leave the 3" thick glass closed and not have to worry about getting my arm blown off by a improvised explosive device sitting on the side of the road or getting shot in the face.
Justin P. Corder TSgt, USAF-TACP

## Slide 7: WHAT IS AT STAKE
DoD’s ability to successfully carry out its mission.
Our troops ability to know their location.
Ultimately, people’s lives.

## Slide 8: ASMO ANALYSIS
Army Spectrum Management Office performed EMI analysis to determine a separation distance between GPS Re-radiators and GPS Receivers.
Utilized L1 frequency of 1575.42 MHz.
Case 1 based on the GPS signal of -130 dBm.
Case 2 based on the GPS signal of -124 dBm.

## Slide 9: CHRONOS GPS Re-radiating UNIT RA-46

## Slide 10: CONFIGUARTION REPRESENTATION
GPS Re-radiator Kit
Amplifier
GPS Receiver
Separation Distance
Receive Antenna
Re-Transmit Antenna
Parameters
Amplifier Gain: 28 dB
Re-transmit antenna gain: 20 dBi
Cable Losses: 0 dB
GPS Antenna Gain case 1: 0 dBi
GPS Antenna Gain case 2: 2.1 dBi
Free Space Path Loss (dB) = 20 Log D (meters) + 20 Log F (MHz) -27.55

## Slide 11: EMI ANALYSIS RESULTS CASE 1
1 Meter Ex: -130 dBm + Antenna gain (s) + Amp Gain – Free space Loss = -118.3 dB
Distance Separation Between GPS receiver and re-transmitter | Signal Strength of the re-radiated signal at the GPS Receiver | Re-transmitter Antenna Gain | Receiver Antenna Gain | Power Output from Re-transmitter (out of the amplifier before antenna) | GPS Frequency L1 | Free Space Path Loss
1 meter | -118.3 dBm | 20 dBi | 0 dBi | -102 dBm | 1575.42 MHz | 36.38 dB
2 meters | -124.4 dBm | 20 dBi | 0 dBi | -102 dBm | 1575.42 MHz | 42.40 dB
3 meters | -127.9 dBm | 20 dBi | 0 dBi | -102 dBm | 1575.42 MHz | 45.9 dB
4 meters | -130.4 dBm | 20 dBi | 0 dBi | -102 dBm | 1575.42 MHz | 48.4 dB
5 meters | -132.3 dBm | 20 dBi | 0 dBi | -102 dBm | 1575.42 MHz | 50.3 dB
6 meters | -133.9 dBm | 20 dBi | 0 dBi | -102 dBm | 1575.42 MHz | 51.9 dB
7 meters | -135.2 dBm | 20 dBi | 0 dBi | -102 dBm | 1575.42 MHz | 53.2 dB
8 meters | -136.4 dBm | 20 dBi | 0 dBi | -102 dBm | 1575.42 MHz | 54.4 dB
9 meters | -137.4 dBm | 20 dBi | 0 dBi | -102 dBm | 1575.42 MHz | 55.4 dB
10 meters | -138.3 dBm | 20 dBi | 0 dBi | -102 dBm | 1575.42 MHz | 56.3 dB
11 meters | -139.2 dBm | 20 dBi | 0 dBi | -102 dBm | 1575.42 MHz | 57.21 dB
12 meters | -139.9 dBm | 20 dBi | 0 dBi | -102 dBm | 1575.42 MHz | 57.96 dB
13 meters | -140.6 dBm | 20 dBi | 0 dBi | -102 dBm | 1575.42 MHz | 58.66 dB

## Slide 12: EMI ANALYSIS RESULTS CASE 2
Distance Separation Between GPS receiver and re-transmitter | Signal Strength of the re-radiated signal at the GPS Receiver | Re-ransmitter Antenna Gain | Receiver Antenna Gain | Power Output from Re-transmitter (out of the amplifier before antenna) | GPS frequency L1 | Free Space Path Loss
1 meter | -110 dBm | 20 dBi | 2.1 dBi | - 96 dBm | 1575.42 MHz | 36.3 dBm
2 meters | -116.3 dBm | 20 dBi | 2.1 dBi | - 96 dBm | 1575.42 MHz | 42.4 dBm
3 meters | -119.8 dBm | 20 dBi | 2.1 dBi | - 96 dBm | 1575.42 MHz | 45.9 dBm
4 meters | -122.3 dBm | 20 dBi | 2.1 dBi | - 96 dBm | 1575.42 MHz | 48.4 dBm
5 meters | -124.2 dBm | 20 dBi | 2.1 dBi | - 96 dBm | 1575.42 MHz | 50.3 dBm
6 meters | -125.8 dBm | 20 dBi | 2.1 dBi | - 96 dBm | 1575.42 MHz | 51.9 dBm
7 meters | -127.1 dBm | 20 dBi | 2.1 dBi | - 96 dBm | 1575.42 MHz | 53.2 dBm
8 meters | -128.3 dBm | 20 dBi | 2.1 dBi | - 96 dBm | 1575.42 MHz | 54.4 dBm
9 meters | -129.3 dBm | 20 dBi | 2.1 dBi | - 96 dBm | 1575.42 MHz | 55.4 dBm
10 meters | -130.2 dBm | 20 dBi | 2.1 dBi | - 96 dBm | 1575.42 MHz | 56.3 dBm
11 meter | -131.1 dBm | 20 dBi | 2.1 dBi | - 96 dBm | 1575.42 MHz | 57.2 dBm
12 meters | -131.8 dBm | 20 dBi | 2.1 dBi | - 96 dBm | 1575.42 MHz | 57.9 dBm
13 meters | -132.5 dBm | 20 dBi | 2.1 dBi | - 96 dBm | 1575.42 MHz | 58.6 dBm
14 meters | -133.2 dBm | 20 dBi | 2.1 dBi | - 96 dBm | 1575.42 MHz | 59.3 dBm
15 meters | -133.8 dBm | 20 dBi | 2.1 dBi | - 96 dBm | 1575.42 MHz | 59.9 dBm
16 meters | -134.3 dBm | 20 dBi | 2.1 dBi | - 96 dBm | 1575.42 MHz | 60.4 dBm
17 meters | -134.9 dBm | 20 dBi | 2.1 dBi | - 96 dBm | 1575.42 MHz | 60.9 dBm
18 meters | -135.4 dBm | 20 dBi | 2.1 dBi | - 96 dBm | 1575.42 MHz | 61.4 dBm
19 meters | -135.8 dBm | 20 dBi | 2.1 dBi | - 96 dBm | 1575.42 MHz | 61.9 dBm
20 meters | -136.3 dBm | 20 dBi | 2.1 dBi | - 96 dBm | 1575.42 MHz | 62.4 dBm

## Slide 13: EMI ANALYSIS RESULTS CASE 2 CONTINUED
Distance Separation Between GPS receiver and re-transmitter | Signal Strength of the re-radiated signal at the GPS Receiver | Re-transmitter Antenna Gain | Receiver Antenna Gain | Power Output from Re-transmitter (out of the amplifier before antenna) | GPS Frequency L1 | Free Space Path Loss
21 meters | -136.73 dBm | 20 dBi | 2.1 dBi | - 96 dBm | 1575.42 MHz | 62.83 dBm
22 meters | -137.13 dBm | 20 dBi | 2.1 dBi | - 96 dBm | 1575.42 MHz | 63.23 dBm
23 meters | -137.52 dBm | 20 dBi | 2.1 dBi | - 96 dBm | 1575.42 MHz | 63.62 dBm
24 meters | -137.88 dBm | 20 dBi | 2.1 dBi | - 96 dBm | 1575.42 MHz | 63.98 dBm
25 meters | -138.24 dBm | 20 dBi | 2.1 dBi | - 96 dBm | 1575.42 MHz | 64.34 dBm
26 meters | -138.58 dBm | 20 dBi | 2.1 dBi | - 96 dBm | 1575.42 MHz | 64.68 dBm
27 meters | -138.91dBm | 20 dBi | 2.1 dBi | - 96 dBm | 1575.42 MHz | 65.01 dBm
28 meters | -139.22 dBm | 20 dBi | 2.1 dBi | - 96 dBm | 1575.42 MHz | 65.32 dBm
29 meters | -139.53 dBm | 20 dBi | 2.1 dBi | - 96 dBm | 1575.42 MHz | 65.63 dBm
30 meters | -139.82 dBm | 20 dBi | 2.1 dBi | - 96 dBm | 1575.42 MHz | 65.92 dBm
31 meters | -140.11 dBm | 20 dBi | 2.1 dBi | - 96 dBm | 1575.42 MHz | 66.21 dBm

## Slide 14: RECOMMENDATIONS
Modify the existing NTIA regulations for utilization of the GPS Re-radiating devices.
Due to current regulations, resellers of the GPS Re-radiators are hesitant to sell GPS Re-radiating equipment to DoD elements.
Reassure resellers of the GPS Re-radiators that purchase by DoD forces for OCONUS use is allowed under the current regulations.
Make allowances for DoD to purchase GPS Re-radiators for its use Nationally for test and training on military bases and installations.