## Slide 1: NOAA GOME-2 Cal/Val Plans
L. Flynn, Co-Chair
Atmospheric Chemistry POP
with input from S. Kondragunta, Z. Zhang, Y. Pachepsky and the GOME-2 website

## Slide 2: Outline
Status
  Calibration and Format documents obtained
  Sample and Proxy Measurements obtained
Measurements
Calibration and Characterization Parameters
Validation, Soft Calibration and Maintenance
Product Development and Implementation Status
Further product development plans and need for support

## Slide 3: Global Ozone Monitoring Experiment (GOME-2)
Notes: The instrument is almost a carbon copy of the GOME concept: A scan mirror directs the light reflected from the Earth atmosphere into the instrument telescope. Additionally, the scan mirror can point to the Sun diffuser and to internal calibration light sources. Behind the entrance slit of the telescope the light is collimated onto a Brewster/pre-disperser prism configuration to split from the main light beam a s- and p-polarized light beam, which is directed to the Polarization Measurement Unit (PMU). Subsequently the main beam is separated with respect to the spectral coverage of the four main channels by a channel separator prism and a dichroic filter. Finally the light is dispersed by four gratings and focused by four objectives onto a silicon linear detector array in the Focal-Plane Assembly.
To achieve an accurate radiometric in-orbit calibration of the instrument, GOME-2 has two internal calibration light sources, one of which offers well-isolated spectral lines in the required wavelength range and a white light source (WLS) for the broadband continuum. The WLS, which is not part of the GOME calibration unit, is used to monitor the etalon that is present on the cooled Reticon detectors, due to freezing water vapor . Pt/Cr/Ne hollow cathode discharge lamp.

## Slide 4: GOME-2 Measurements
Vis4 (590-690nm) Vis3 (401-600) UV2 (311-403nm) UV1b (290-315nm)
  Every 3/16 S (80 KM by 40 KM at nadir)
  6S, 24 + 8 measurement, 1920 km cross-track
UV1a (240-290 nm)
  1.5 S 3 cross track measurement plus 1 fly-back.
  More frequent sample during IOV
Vis3 has visible wavelengths for NO2 and better aerosol products
PMD 10 KM by 40 KM (290-800nm)
  Six of the 15 channels mimic TOMS wavelengths
3-Minute Granules contain 30 scans, 960 spectra
Solar Spectrum at least once per day
Notes: GOME-2 contains two spectrometers - one to measure the radiance component of light that is reflected from the Earth atmosphere in the direction of the satellite (the main channels), in the spectral range 240-790 nm with a resolution of 0.24-0.53 nm and another spectrometer to characterize simultaneously the state of polarization of the same spectrum (the Polarization Measurement Unit). The instrument is almost a carbon copy of the GOME concept: A scan mirror directs the light reflected from the Earth atmosphere into the instrument telescope. Additionally, the scan mirror can point to the Sun diffuser and to internal calibration light sources. Behind the entrance slit of the telescope the light is collimated onto a Brewster/pre-disperser prism configuration to split from the main light beam a s- and p-polarized light beam, which is directed to the Polarization Measurement Unit (PMU). Subsequently the main beam is separated with respect to the spectral coverage of the four main channels by a channel separator prism and a dichroic filter. Finally the light is dispersed by four gratings and focused by four objectives onto a silicon linear detector array in the Focal-Plane Assembly. The minor changes to the design of the GOME spectrometer may be summarized as followed: 1. GOME-2 has a more complex Polarization Measurement Unit (PMU) than GOME, which measures simultaneously s- and p-polarized light on a spectral resolution between 2.8 nm at 312 nm and about 40 nm at 790 nm.
2. To achieve an accurate radiometric in-orbit calibration of the instrument, GOME-2 has two internal calibration light sources, one of which offers well-isolated spectral lines in the required wavelength range and a white light source (WLS) for the broadband continuum. The WLS, which is not part of the GOME calibration unit, is used to monitor the etalon that is present on the cooled Reticon detectors, due to freezing water vapor . 3. The maximum swath width is increased to 1920km across track in order to address the user requirement of global coverage in one day. In conjunction with this change the scan speed is adjusted to minimise the effect of oblique viewing and provide a constant scan rate on the ground. However, the scans is completely reprogrammable in-flght allowing an almost unlimited choice of scan profiles. 4. The width of the entrance slit is increased from 0.1 mm for GOME to 0.2 mm fro GOME-2, which avoids the spectral undersampling of the spectrometer. 5. The coating of the different optical elements is changed to reduce both a steady out-gassing of the coating experienced with GOME and the straylight component measured by the detectors. 6. Due to a different groove profile of the gratings the polarization sensitivity of the main channels is considerable lower than for GOME. More details on the GOME spectrometer concept can be found on our GOME-website. The optical layout of the GOME-2 spectrometer. The integration time can be separately set for each channel; in channel 1 and 2 it is possible to sub-divide the channel in two parts (called 'band 1a', 'band 1b' and 'band 2a, 'band 2b' respectively) having separate integration times. It is anticipated that a default integration time of 0.1875ms will be used in all channels with two exceptions where longer integration times are needed because of low light intensity: (i) Band 1a has a default integration time of 1.5 seconds (yielding three spectra per scan and one from the fly-back with the possibility of co-adding spectra to improve signal to noise characteristics). (ii) The integration time for all channels will be increased for low solar elevations (high solar elevation angles). For the 1920km swath, the maximum temporal resolution of 187.5ms for the main channels (23.4ms for the PMD channels) corresponds to a maximum ground pixel resolution (across-track x along-track) of 80km x 40km (10km x 40km for the PMDs) in the forward scan.

## Slide 5: http://ftp.sron.nl/index.php?option=com_content&task=view&id=193&Itemid=125
Band Pixel centers nm Pixels Pixel FWHM nm 0 Spare 1 311.8-314.3 5 3.1 2 316.9-318.8 4 3.3 3 321.5-329.3 12 3.5 4 330.8-334.6 6 3.8 5 336.2-363.1 44 4.8 6 380.3-383.9 4 6.1 7 399.8-428.0 19 7.8 8 435.1-552.4 46 12.5 9 552.4-556.2 2 18.7 10 567.9-680.0 24 25.2 11 743.1-750.8 4 38.5 12 758.8 1 40.2 13 792.4 1 43.9 14 Spare
Proposed PMD Channels

## Slide 6: Input Required by the Algorithms
Standard Ozone Wavelengths or DOAS Spectral Windows
Radiance (corrected for calibration, polarization, non-linearity and dark current)
Irradiance (corrected for calibration, polarization, goniometry, Doppler, non-linearity, and dark current)
Wavelength Scales for Earth and Solar
Geolocation information
Satellite viewing angles and solar zenith and azimuth angles
Ancillary data sets (climatology, forecast or retrieved)

## Slide 7: Calibration and Validation Checks
Wavelength Scale/Shape
  Solar Lines, Neon/Argon Lamp
Noise, offsets, and transients
  Night-side and continuity
IB and OOB stray light
  Correlation with reflectivity
  Filling in of solar lines in Earth view
Polarization correction
  w/wo clouds, PMD correlation with changes
Reflectivity distribution
Total ozone pairs (A, B and D)
Initial and final residuals
Intercomparisons with Satellite and GB

## Slide 8: Internal and Soft Calibration and Validation Sequence for Total Ozone
1. Check 331-nm reflectivity channel calibration by using global distributions of reflectivity – minimum ocean (4%) and land (1%) reflectivity, maximum global reflectivity and ice radiances (Greenland and Antarctica).
2. Check agreement between 360-nm reflectivity and 331-nm reflectivity for scenes with reflectivity greater than 80%.
3. Compute total ozone for nadir measurements from B-pair (317.5-nm and 331-nm) in the tropics and compare to expected values.
4. Check agreement of other ozone sensitive channels/pairs with the B-pair results.
5. Check agreement between zonal means at each satellite view angle and the nadir zonal means.
6. Compare ozone and reflectivity results for different channels and pairs as functions of solar zenith angles and reflectivity.
Methods developed at NASA GSFC over the last 30 years.
Notes: Pair Justification
Spectral Discrimination
Ice Radiances
NASA GSFC work over the last 30 years.
Algorithms are designed to use ratios, and ratios of ratios.

## Slide 9: Products Under Development
Total Ozone: V8, PMD V8, and DOAS
Profile Ozone: V8, SAF, GSFC/SAO
SO2 estimates: V8, UMBC, OMI
Trace gases (NO2 etc.): AQ, SAF, OMI/SAO
Aerosols: V8, SAF, PMD V8, OMI/UMBC, AQ
Cloud height: SAF, OMI O2-O2 or Ca H&K
SAF = Satellite Applications Facility
AQ = Air Quality R&D in StAR
V8 = PSDI/GSDI algorithm implementation
Notes: Ozone SAF http://o3saf.fmi.fi/atuotteet.html

## Slide 10: Near Real Time Products from GOME-2
Data Acquisition (MetOP)
NRT Level 0-1 Processing (EUMETSAT)
Offline Processing (Ozone SAF and others)
NRT Level 1-2 processing (NESDIS)
NRT Level 1-2 processing (Ozone SAF)
Raw data
Level 1B
Total and profile ozone, Clear-sky UV, aerosols
Total Ozone
Profile Ozone
Aerosol Index
Nitrogen dioxide
Sulfur dioxide
Formaldehyde
Aerosol Optical Depth*
Bromine and Chlorine compounds*
By 2007
By 2008
*funding anticipated

## Slide 11: V8 TOZ progress
Read in Earth sample radiance at selected channels
Read in Solar irradiance at selected channels
Adjusted wavelength scale and computed albedos
Created Look-Up Tables with bandpasses
Read in SZA, SAA and SVA
Created flags and formatted output file
Ran with test granules in pipeline processing
Notes: Were asymmetric bandpasses used?

## Slide 14
Notes: Need to use asymmetric bandpasses.

## Slide 15: V8 Profile Progress
OMI Nadir Retrievals
Similar input to Total Ozone
  more wavelengths and data from Channel 1 and Channel 2
Off-nadir retrievals under development
Complications from Channel 1a
  large FOV / different integration times
    Sample short integration data during IOV
  Signal to Noise Ratio is poorer
  Stray Light may need corrections
  Polarization correction is from extrapolation

## Slide 16: DOAS Trace Gas Products
Retrieved species | Fitting window | Reference spectra
O3 | 325 - 335 nm | O3, Ring
O3, NO2 | 425 - 450 nm | O3, NO2, Ring
HCHO | 336.5 - 357.5 nm | HCHO, O3, NO2, BrO, O4, Ring
BrO | 345.6 - 359.0 nm | BrO, NO2, O3, (OClO), Ring
SO2 | 313.5 - 327.0 nm | SO2, O3, Ring
OClO | 357.0 - 381.5 nm | OClO, NO2, O4
CHO-CHO may be retrievable in the 430 – 460 nm fitting window.

## Slide 17: Total Ozone Products
May need some support for contractor to perform and implement soft calibration analysis outlined on next slide if Level 1b calibration is not of high quality
May need some support for validation
  Comparisons to SBUV/2 Total Ozone
  Comparisons to OMI and TOMS TOZ
  Comparisons to Ground-based Dobson
  Comparisons to other solar irradiance spectra
Need support to implement high resolution TOZ from PMD

## Slide 18: Future Tasks for GOME-2
TOZ
  Complete Documentation & Implementation (S)
  Provide Maintenance and Adjustments (P)
  Perform Validation of TOZ (P)
  Adapt and Implement V8 PMD product (N)
Profile Ozone
  Complete Adaptation & Implementation (P)
DOAS Trace Gases and Aerosols
  Complete DOAS Adaptation and Implementation (P)
  Implement improved SO2 product (P)
  Implement improved aerosol product (P)
S Supported, P Partially Supported, N Funding Needed
Assumes Base support for operational product processing
and continued Air Quality development support.

## Slide 19: Trace Gas and Aerosol Products from MetOP GOME-2 Mitch Goldberg, Shobha Kondragunta, Lawrence. E. Flynn NOAA/NESDIS Center for Satellite Applications and Research & James. J. Szykman and Richard Scheffe Environment Protection Agency NERL/ORD

## Slide 20: MetOP GOME-2
GOME-2
  July 17, 2006 launch on MetOP-1into 9:30 AM orbit
  UV/VIS sensor (240 nm – 790 nm) for atmospheric chemistry and air quality
    Pixel resolution 40 X 80 km2. Polarization measurements at select wavelengths at 40 X 10 km2. Very useful for retrieving aerosol properties
    Will provide tropospheric amounts of ozone, nitrogen dioxide, sulfur dioxide, formaldehyde, glyoxal, aerosols with ability to distinguish between dust/smoke vs urban/industrial aerosols. Most of these products are EPA designated criteria pollutants for air quality
Heritage instrument: ERS-2 GOME-1
  1995-2002
  DOAS algorithms developed to make use of hyperspectral coverage. Algorithms easily adaptable to GOME-2
  Data widely used in air quality modeling and assessment. Applications limited to monthly and seasonal time scales due to large footprint of GOME-1 (~250 km)
Reichter et al. (Nature, 2005) using GOME data showed that NOxemissions in the U.S. are decreasing but increasing in Asia. EPA wants to extend this record to 2030 with GOME-2 data to track newly implemented Clean Air Interstate Rule
US
China

## Slide 21: User Needs
EPA
  Track Clean Air Interstate Rule (CAIR). Are NOx and SO2 controls working? Is visibility improving in our national parks?
    Long-term monitoring from satellites critical to track trends
NWS
  Improve air quality forecast accuracy
    Near real term monitoring from satellites critical for satellite data assimilation
National NOx and SO2 Power Plant Emissions: Historic and Projected with CAIR
474 Counties with a population of 159M in non-attainment
Notes: This and the next slide is a summary of user needs that came out of the air quality breakout session at the 2003 GOES-R users conference.

## Slide 22: EPA Timeline for Use of GOME-2 data for Air Quality Applications involves on-going collaboration with NOAA & NASA
Applications Research
Validation & Verification
Applications Demonstration
2004 - 2008
2008- 20012
2012 and beyond
SCIENCE
Nationwide
Data
APPLICATIONS
Implementation as
Air Quality
Management Tool (mature products)
On-going involvement from EPA, State, Local, and Tribal Air Quality Management Organizations
On-going studies on use of
GOME, SCIA and OMI data.
Demonstrate Linkages of
Regional Scale Satellite
Measurements to In-situ
measurements and emission
inventories.
Evaluate GOME-2 operational products.
Intercomparison and continuity studies with heritage sensors. Evaluation of first 5 year of GOME-2 data for trends.
On-going assessment of air quality trends with
GOME-2 data against traditional benchmark data sets and incorporation into as an indicator for accountability.
GOME, SCIA, OMI
(NASA) sensors provide
prototype data sets for
GOME-2. (Ozone, NO2,
SO2, Aerosol, HCHO)
NOAA/NESDIS starts production of air quality GOME-2 data products.
GOES-R and potential future NASA Geostationary
tropospheric chemistry missions.
Operations

## Slide 23: Shortfalls that Must be Met
To meet user requirements, NESDIS has to invest substantial effort towards algorithm and product development
  Acquire capabilities,
  Use Aura OMI and Envisat SCIAMACHI data as risk reduction,
  Collaborate with the group at Harvard Smithsonian Astrophysical Organization (SAO) which developed OMI trace gas algorithms,
  Collaborate with NASA scientists who developed OMI total ozone and aerosol product algorithms (this falls under NASA Research to Operations activity),
  Coordinate with the users on product development and user application