## Slide 1
Instrumented Surface Sub
DOE Project (DE-FC26-03NT41782)
Downhole Technology, Ltd.

## Slide 2: Project Objective
To refine and field test the Instrumented Surface Sub, and collect critical drilling data during the field tests to begin development of algorithms to process these critical data so penetration rate can be optimize and BHA life can be maximized.

## Slide 3: What Is Instrumented Sub
Data Collection Device
Fits In Drill String Below Top Drive
Measures Critical Drilling Parameters
Wireless Communications To Computer
Enhancement To Drilling Performance
Prevents Damage To Drill String & BHA

## Slide 4: Instrumented Surface Sub

## Slide 5: Recorded Drilling Parameters
String Weight (Direct Measurement)
Rotary Torque (Direct Measurement)
Rotary Speed
String Vibration
  Tri-axial Accelerometer Package
Drill String Surface Pressure
Mud Temperature

## Slide 6: Sub Electronics

## Slide 7: Sub Specifications
Length
Diameter
Top Connection
Bottom Connection
Power Source
Batter Life
Communications
Transmission Rate
20 in. Shoulder to Shoulder
13.5 in. (Cover Flanges)
7-5/8 API Box
7-5/8 API Pin
Internal Battery
(Life 40 to 48 hours)
Wireless (900 KHz)
38,400 bits/sec

## Slide 8: Sub Specifications (Con’t)
Max String Weight
Max Torque
Pressure
Temperature Range
Max Vibration
Rotary Speed
0-1,300,000 lbf
0-100,000 ft-lbf
0-8000 psi
32-400 oF
50 g’s
0-200 rpm

## Slide 9: What Do We Want To Accomplish
Improve Drilling Data
  Direct measurement vs inferred
  Better resolution
Additional Data
  Vibration
  Trend
Present In Meaningful Manner
  Useful To Driller
  Expose Obscure Or Unknown Information
  Automate Changes In Drilling Parameters

## Slide 10: What Do We Need
Top Drive Land Or Offshore Rig
Well To Take Data
Baker MWD (Optional On First Test)
Varying Drilling Conditions
  Increasing Well Depth
  Changing Formations
  Difficult BHA Conditions (e.g. Stick Slip)
Space To Setup Computer

## Slide 11: What We Provide
Instrumented Drill Sub
Expertise To Oversee Installation
Addition Of VSSsm Service To Baker MWD
Operator To Monitor & Service System
Improved Drilling Data
Drill Graph Services

## Slide 12
Noble Corporation
13135 South Dairy Ashford, Suite 800
Sugar Land, Texas 77478
(281) 276-6100
NYSE: NE
www.noblecorp.com
The End