## Slide 1: Comparison of v3.1.9 and v3.5.0 AIRS Column Ozone with TOMS AIRS Science Team Meeting Greenbelt, Maryland March, 2004
Bill Irion, Sung-Yung Lee, Bjorn Lambrigtsen, Mike Gunson (JPL)
Mike Newchurch, Mohammed Ayoub (UAH)

## Slide 2: Change in ozone channels V3.1.9 correlation of AIRS-TOMS difference with skin temperature suggested avoiding CO2 lines in O3 channels.

## Slide 3
Comparison of AIRS to TOMS total column using new channel selection
Sept 6, 2002 focus day, v3.2.7 processing
Note: TOMS retrieved information on only about half the globe on this day.
(AIRS - TOMS) / TOMS Median difference % (1) | Original O3 channels | Modified O3 channels
All pixels | 5.3 ± 6.5 | 3.4 ± 6.8
> 99% land | 8.7 ± 7.3 | 4.5 ± 7.9
> 99% ocean | 3.7 ± 4.9 | 2.8 ± 5.7

## Slide 4
Modified ozone channels
Land Fraction
Skin temperature (K)
(AIRS - TOMS)/TOMS (%)
Sensitivity of ozone column to skin temperature
Sept. 6, 2002 focus day, 40°S - 40°N, V3.2.7
Slope of (AIRS - TOMS) / TOMS vs Tskin (% / K) (1) | Original O3 channels | r | Modified O3 channels | r
All pixels | 0.225 ± 0.003 | 0.36 | 0.109 ± 0.004 | 0.16
> 99% land | 0.078 ± 0.008 | 0.10 | 0.002 ± 0.008 | 0.002
> 99% ocean | 0.204 ± 0.006 | 0.23 | 0.160 ± 0.008 | 0.16
Skin temperature (K)
Land Fraction
Original ozone channels

## Slide 5: v3.1.9 and v3.5.0 comparison with TOMS January 1-31, 2003
Type 0 retrievals
Daytime granules
V3.1.9: Avg = 5.8 ± 4.6 (1); N = 964428
V3.5.0: Avg = 3.7 ± 4.7 (1); N = 670302

## Slide 6: Conclusions
New ozone channels produce significantly improved agreement with TOMS under v3.2.7 processing for 9/6/2002 focus day.
Lowered yield for V3.5.0, ~30% decrease in Type 0 40°S - 40°N ocean retrievals from v3.1.9 to v3.5.0.
v3.5.0 ocean retrievals in better agreement with TOMS than v3.1.9 on average, but regional differences remain.
Further work
Check land retrievals after Jan 2003 data set has been reprocessed.
Comparison of tropospheric and lower stratospheric retrievals with ozonesondes (in collaboration with Mike Newchurch of UAH). Current data set includes dedicated ozonesondes from Huntsville and Chesapeake Bay Lighthouse, plus vicarious sonde/Dobson/Brewer/lidar measurements from 143 stations.
Preliminary evaluations of polar ozone retrievals during polar night, with studies of the vortex morphology entering springtime daylight.