## Slide 1: Allergens and the Confectionery Industry
Alison Bodor
Vice President Regulatory and Scientific Affairs

## Slide 2: National Confectioners Association
Over 300 manufacturing confectionery company members
Interest in allergens for past 15 years
Participant in Food Allergy Issues Alliance
Goal is to best protect the consumer

## Slide 3: Topics to Cover
Industry Overview
Circumstances that influence use of advisory labeling
Guidance for industry
Relevance of company size
Unique challenges

## Slide 4: Industry Overview

## Slide 5: Major Food Allergens used in candy
Peanuts
Milk
Eggs
Soy (lecithin)
Wheat
Fish (gelatin, omega-3 fa)
Almonds
Walnuts
Macadamia Nuts
Pecans
Cashews
Hazelnuts
Pistachios
Coconut

## Slide 6: What manufacturing circumstances prompt manufacturers to place advisory statements on a food label?

## Slide 7: Influencing Factors
Ingredient procurement
Physical characteristics of allergen
Manufacturing one or more allergens in the same facility
Manufacturing one or more allergens on the same equipment
Chocolate GMPs

## Slide 8: Particulate Matter vs Readily Dispersible Proteins
Particulate
Peanuts, Tree nuts
Particulate matter gets caught in equipment
No certainty of cleaning technique, testing not appropriate
Risk of significant quantity of protein reaching consumer in small serving
Dispersible Proteins
Milk, whey, soy, egg, etc
Residual levels affected by type of candy, time, equipment
Bound by chocolate; impossible to rid from some systems

## Slide 9: Shared Facility
Very few candy companies in the industry have dedicated facilities that isolate allergens
Many allergens often used in same facility
Barriers to cross contact not foolproof
Risk of human error, even with employee education and allergen control plans in place
Dedicated facility is not a realistic expectation.

## Slide 10: Shared Equipment
Most confectioners use the same equipment to produce many different candies
Constraints include space, cost, efficiencies
Those who use shared equipment have an allergen clean-up strategy and are more likely to use advisory labeling.
Dedicated equipment is not a realistic expectation.

## Slide 11: Unavoidable Cross-contact:
Inaccessible Equipment
  Equipment not intended to be dismantled.
  Many systems or components of systems are closed
Shared equipment that cannot be wet cleaned
  For chocolate operations, carbon steel equipment often used. Can be corrosive with water system.
Difficult to achieve certainty
that allergens are eliminated.

## Slide 12: Chocolate
Manufacturing in a Dry Environment

## Slide 13: Water and Pathogens
Chocolate is very viscous and adheres in thick layers to machinery, pipes
  Flushing is very difficult
Chocolate + water = stiffness
These pockets of water can foster microbial growth
Cannot guarantee dryness in system
Basic GMP principle:
Avoid water-cleaning systems for most chocolate equipment
Notes: The uptake of moisture in chocolate can make the product unusable. Chocolate and moisture do not mix. A long standing practice with chocolate manufacturers is that all possible precautions are taken to prevent moisture from getting into the chocolate processing system. Dry cleaning is typically used in many areas of a chocolate plant. Even a trace amount of water will go directly to the sugar particles, form a microscopic syrup film, and cause the chocolate to seize up in a consistency like fudge. In manufacturing, there is a great risk of pockets of wet product to adhere to the inside of piping or tanks causing growth niches for mold and bacteria.

## Slide 14: Dry Clean and Flush
Dry Clean
Depends on accessibility of equipment
Extremely labor intensive
Not able to rid many systems of allergen proteins
Flush
Chocolate clings to pipes
Flushed chocolate must be reworked. Introduces new risk.
Does not eliminate risk of allergen protein.
Does not eliminate need for advisory labeling.

## Slide 15
Mixing and Pre-refining Room

## Slide 16
Liquid Phase Conching

## Slide 17: Chocolate Feed to Enrober

## Slide 18: Typical Points of Cross Contact: Chocolate and Other Confections
Ingredient feed systems, pipes
Conveyors, tunnels
Mixing Equipment
Release agent reservoirs
Tempering units
Depositors
Vacuum cook kettles
Cutting equipment
Wire belts
Rework vessels, grinders
Enrobers
Extruders
Panners
Utensils, gloves, clothes
Wrapping equipment

## Slide 19: Ingredient Procurement
Reliance on operations of suppliers
Carry-forward principle for labeling, if verified
  Multiple peanuts and tree nuts processed by same suppliers
  Dark chocolate with milk protein

## Slide 20: Testing
Use visual inspection and analytical testing to facilitate the design of the clean-up procedure
  Used to validate a sanitation procedure
  Doesn’t measure “hung-up” product that can later dislodge
  Cannot guarantee safety
Need analytical methods for some allergens and validation of other methods.
Industry needs FDA to establish thresholds

## Slide 21: Guidance for Industry: Advisory Allergen Labeling

## Slide 22: Food Allergen Issues Alliance Labeling Guidelines
Recommend using advisory statements for unavoidable cross contact when all of the following exist:
    Allergen presence is documented - visual, analytical, etc.
    Risk is unavoidable even when current GMPs followed
    Allergen present in some, but not all, products
    Presence is potentially hazardous

## Slide 23: Relevance of Company Size
Similar proportion of shared facilities and shared manufacturing lines
Labeling criteria and considerations of small companies similar to medium and large companies
Frequency of advisory labeling is similar, based on limited NCA survey data
Small companies possibly less likely to document presence of allergen via analytical or visual testing
  Issue of resources, expertise?
Small companies = 100 employees or less
Medium companies = 101 to 500 employees
Large companies = 500 to 1000+ employees

## Slide 24: Additional “Alliance” Guidelines:
Advisory statements should be accurate and conspicuous.
Advisory statements should be placed at the end of, or in close proximity to, the ingredient declaration.
When using an ingredient that utilizes an advisory statement, the food processor should carry that statement forward to the label of its food, when risk verified.
Food processors should strive to label the same product consistently, even if produced in different locations or in different package sizes.
Candy companies support...

## Slide 25: Typical Common Advisory Label Approaches for Confectionery
May contain X. (or May contain traces of X.)
Manufactured on equipment that also processes X.
Manufactured in a facility that processes X.

## Slide 26: What do advisory statements on candy mean?
No confectionery industry agreement on levels of risk associated with different statements
An advisory statement is intended to indicate risk to the allergic consumer
An advisory statement -of any kind- means that allergic consumers should not eat the product.

## Slide 27: Challenges
Is it possible to convey a level of risk to the consumer?
Industry needs FDA to establish thresholds/action levels.
How do we communicate risk of a particulate allergen?
Need to account for variability in allergen levels, depending on allergen characteristic, processing system and sanitation capabilities.
Companies will err on the side of over protecting the consumer.

## Slide 28: Additional Confectionery Concerns
Label carryover from ingredient suppliers
  Chocolate with milk or nut proteins
  Peanuts and tree nuts are often processed in same facility
Limited label space / smaller formats
Recommend same labeling for brand manufactured in different plants regardless of manufacturing conditions and size variations.

## Slide 29: Summary:
Advisory labeling is important tool that confectionery manufacturers use to help allergic consumers make an informed choice.