## Slide 1: Annual Refresher Training
Emergency Response

## Slide 2: Fire
Fire is the most potentially devastating emergency in the modern laboratory
Use the smallest quantities of flammable solvents practicable
Store stock quantities in flammable storage cabinets
Separate flammable solvents from sources of ignition/ bunsen burner

## Slide 3: Clothing Fire
A co-worker in your lab has just spilled ethanol. The spill has burst into flame and his clothing has caught fire
Put out the fire: Drop and roll; roll around on the floor to smother the flames
Chill burn with cold water
Seek medical attention, and report the incident to your supervisor

## Slide 4: Lab Bench Fire
A flammable liquid has just spilled onto the bench and has caught fire
Alert people in the laboratory and activate alarm

## Slide 5: Lab Bench Fire, continue
Smother fire or use correct fire extinguisher (only those who have been trained can use the extinguisher)
For wood, paper, cloth, & trash
For gasoline, grease, oil, paint, and flam. liquids
For live electrical equipment

## Slide 6: Lab Bench Fire, continue

## Slide 7: Lab Bench Fire, continue
Stay on exit side of the fire
Report the incident to your supervisor

## Slide 8: Major Lab Fire
Follow these immediate procedures in case of major lab fire:
Alert people to evacuate the area
Activate nearest fire alarm or call for emergency response
Close lab doors to confine fire
Have person who is knowledgeable about the lab and incident ready to assist emergency personnel

## Slide 9: Eye Splash
Working quickly, you flicked open an Eppendorf tube and several droplets of phenol hit your eye
Immediately rinse eyeball and inner surface for 15 minutes
Forcibly hold eye open to insure effective wash behind eyelids
Obtain medical attention
Report the incident to your supervisor

## Slide 10: Chemical Spill
A colleague has just spilled acid on his clothes.
Flood exposed area with running water from faucet or safety shower for at least 5 minutes
Remove contaminated clothing at once
Make sure chemical has not accumulated in shoes
Obtain medical attention, and report the incident to supervisor

## Slide 11: Chemical Spill
You dropped 250 mL bottle of ammonium hydroxide on the floor.
Alert others of the spill
Locate the spill kit in the hallway
Put on the Personal Protective Equipment
Neutralize it with bicarbonate
Collect residue into plastic bag, secure it, and label it a hazardous waste.

## Slide 12: Radiation Spill
You’ve just spilled radioactive material on your lab coat and arm
Remove contaminated clothing
Rinse exposed area thoroughly with soap and water
Obtain medical attention if necessary
Report the incident to your supervisor

## Slide 13: Electrical Outage
If working with chemicals under the fume hood
Cap the container
Close the hood sash
Contact person directing work in the laboratory
Exit building
Meet at designated evacuation spot – parking lot behind the facility

## Slide 14: Security Threats
Identification cards must be worn at all times and visible to all personnel
If you observe someone committing a crime, DO NOT attempt to apprehend or detain the suspect. Try to memorize the physical appearance of the suspect and call 5-111 (Cornell police) or 911

## Slide 15: Security threats, cont.
Non-emergency situations
Call Cornell campus police at 5-1111
Call Bill Shaben at 5-1065 or his cell phone at (607) 280-1506
Emergency situation
Call 911
Call Bill Shaben at 5-1065 or his cell phone at (607) 280-1506

## Slide 16: Our records are good, let’s keep it that way

## Slide 17: All Done!
Make sure you fill out the quiz, sign it, and drop it off in my mailbox for record keeping.
Remember: This is an annual requirement.
SEE YOU NEXT YEAR

## Slide 18: Any Questions?
Contact: Kathie Moh
255-8849
kcm25@cornell.edu