## Slide 1
TL Jones-Lepp
United States Environmental Protection Agency
Office of Research & Development
NERL-Environmental Sciences Division
Environmental Chemistry Branch
Las Vegas, Nevada
Chemical markers of human waste contamination in source waters: A simplified analytical approach

## Slide 2: Introduction
Giving public water authorities a tool to monitor and measure levels of human waste contamination of waters simply and rapidly would enhance public protection.
Chemicals shed in feces and urine might be used to detect human waste contamination of environmental waters.
  Sterols
  Bile acids
  Urobilin
    Finding human-use drugs affiliated with
    urobilin can help define the waste as human.
      Azithromycin (antibiotic) and methamphetamine (substance of abuse) were detected

## Slide 3: Experimental
Samples
  Grab samples collected, 1L or less, keep cool, above freezing but < 4oC until extraction w/in 24-hrs
  pH adjust to < 3.0 with 12N HCl
Solid phase extraction
  OASIS HLB cartridges [Waters Corporation (Milford, MA)]
    6-mL capacity, 0.2 g, 30-µm
    Prep cartridges 5 mL methanol followed by 5 mL DI water at a rate of 1 mL/min
    Load samples, 500 mL, into 60-mL reservoirs (60 mLs at a time); start extractions w/ pump at a rate of 4 mL/min
    Dry samples, via pump, for < 5min.
    Extract with 40 mL methanol:1%acetic acid at a rate of 1mL/min.
    Nitrogen blow-down extract to 0.5 mL – ready for LC/MS analysis.

## Slide 4: Experimental con’t
µLC-electrospray-ion trap mass spectrometer (ThermoQuest Finnigan LCQTM
ES-ITMS
positive ionization mode
Screening - scanned from 120 to 830 amu (full-scan mode)
Heated capillary - 215°C
For quantifying and confirming - Two other modes, selected ion monitoring (SIM) and collision-induced dissociation (CID), were used.
HPLC
C18 RP, 5 µm particle size, 150 × 3.2 mm liquid chromatography column
  flow rate of 0.40 mL min–1, and a 40:60 split after the column, such that 40% of the flow (160 µL min–1) goes to the ES-ITMS
Mobile phase: A: 99% water/1 mM ammonium acetate/0.1% acetic acid/1% methanol;
B: 98% methanol/1 mM ammonium acetate/0.1% acetic acid/2% water.
  100% mobile phase A (hold for 1 min) to 100% mobile phase B (hold for 5 min) over a 20-min gradient, with a 5-min equilibrium between runs.

## Slide 5: Experimental cont
Limits-of-detection - Using regression analysis on the data obtained from analyzing urobilin at four different concentrations, using full scan mode, the LOD for urobilin was calculated as 32 pg (r2 = 0.999) on-column.
CID – Collision energy = 30%

## Slide 6: Sampling Sites
Southwest – 1 site in Southern Nevada
Great Lakes – 2 sites on Lake Michigan
New England – 18 sites
  9 in Maine
  9 in Connecticut

## Slide 7: Southern Nevada – 1 site

## Slide 8: Great Lakes – 2 sites Lake Michigan beach site 1 (Silver Beach) Lake Michigan beach site 2 (Washington Beach)
Sample | Urobilin Azithromycin ng/L ng/L | n
Lake Michigan beach site 1 (Silver Beach) June 29, 2004 July 13, 2004 July 27, 2004 August 17, 2004 September 8, 2004 | nd nd nd nd nd nd nd nd no sample | 3 2 2 2 0
Lake Michigan beach site 2 (Washington Beach) June 29, 2004 July 13, 2004 July 27, 2004 August 17, 2004 September 8, 2004 | no sample nd nd nd nd nd nd nd nd | 0 2 2 2 2

## Slide 9: New England – Region 1 Maine 9 sites
Sample | Urobilin ng/L | Azithromycin ng/L | n
AA26900a – Sanford WWTP AA26900b laboratory duplicate AA26901 400 ft downstream Sanford WWTP AA26902a2 Yarmouth POTW AA26902b laboratory duplicate 2 AA26903 Royal River Landing AA26904 Lewiston WWTP AA26905 Androscoggin River 0.8 mi downstream Lewiston WWTP AA26906 South Portland WWTP AA26907 Fore River - marina AA26909 Hampden boat landing | † † 33 11 15 316 11 21 295 16 52 | 77 75 47 nd nd † nd † 41 † 4 | 1 1 1 1 1 1 1 1 1 1 1
nd = non-detect; † positive MS/MS identification, but below LOQ; 2 Methamphetamine detected: 5 ng/L.

## Slide 10
S. Portland Maine WWTP & Fore River Marina
AA26906 AA26907

## Slide 11: Yarmouth Boat Landing & Yarmouth POTW AA26903 AA26902
NOTE: Yarmouth water supply tested positive for coliform Aug and Oct 2002.
Samples were collected Nov 2002. Royal River Yarmouth Town Landing same area.

## Slide 12: Hampden Boat Landing

## Slide 13: New England – Region 1 Connecticut 9 sites
Sample | Urobilin ng/L | Azithromycin ng/L | n
AA29823 – 1.64 miles downstream Manchester WWTP AA29824 – rural stream no housing in the immediate area AA29825 – densely populated 60% stream flow wastewater 1.25mi upstream AA29826 – stream flow 70% wastewater AA29827 -- stream flow 90% wastewater AA29828 -- collected 0.8 km downstream from a senior housing condominium complex, which has its own small WWTP AA29829 0.65 mi from WWTP AA29830 field duplicate of 29829 but collected 15 min apart AA29831 – 2mi downstream WWTP – failed septic systems 90% wastewater AA29832 – 2mi downstream WWTP – stream flow 40 % wastewater Control blank | † nd 16 nd † nd nd 42 17 22 nd | 13 nd 5 39 34 2 15 23 nd nd nd | 1 1 1 1 1 1 1 1 1 1 1
None of the Connecticut samples were collected directly from WWTPs. Most were located 1 km or greater from WWTP sewage outfalls, yet both urobilin and azithromycin were detected in some samples.
nd = non-detect; † positive MS/MS identification, but below LOQ

## Slide 14: Conclusions
Detection of urobilin, along w/ a human-use drugs can equivocally show that human waste is entering a water source.
Tertiary/secondary treatment does not seem to efficiently remove azithromycin, as evidenced by its detection at both the Sanford and Portland WWTPs, as they both have similar environmental loadings, 0.5 kg/yr and 0.6 kg/yr
Future Research
  Investigate correlations between urobilin, nitrate, and coliform levels using principal component analysis

## Slide 15: NOTICE
Although this work was reviewed by EPA and approved for publication, it may not necessarily reflect official Agency policy. Mention of trade names or commercial products does not constitute endorsement or recommendation for use.
Acknowledgments
Dr. Y Miyabara, Shinshu University - Education and Research Center for Inlandwater Environment, for his very thoughtful discussions regarding urobilin as a human waste marker; Dr. Jaci Batista, University of Nevada-Las Vegas for sharing Southern Nevada site information; Mr. Peter Philbrook, USEPA Region 1, for sharing his environmental extracts; and Ms. Elizabeth Sams, USEPA ORD/NHEERL, for sampling throughout the summer 2004, at Lake Michigan.