## Slide 1: What’s a ROPS?
ROPS - Rollover
Protective Structure
During an overturn
a ROPS and seat belt
hold the operator in
a “frame of safety.”
ROPS

## Slide 2: Demonstrating how a ROPS works
ground
frame of safety
ROPS
overturned
model tractor
seat belt
steering wheel
ROPS
simulated seat belt
simulated tractor driver (a raw egg)

## Slide 3: How a ROPS and seat belt work
During an overturn the operator stays
within the ROPS “frame of safety.”
ROPS
seat belt
ROPS
A fastened seat belt holds the
operator on the tractor seat.

## Slide 4: Living dangerously (no ROPS, no seat belt)
steering wheel
tractor
seat
simulated
tractor driver
(a raw egg)
scale model tractor

## Slide 5: An overturn without a ROPS
x
x
overturned model
tractor
ground
simulated tractor driver
(crushed egg)

## Slide 6: Overturns without ROPS are deadly
Without a ROPS and seat belt
the operator is unprotected
during an overturn.
During a recent six-year period, 76 Kentucky
farmers died when their tractors overturned. ROPS and seat belts could have saved all 76.

## Slide 7: Partially protected (ROPS but no seat belt)
scale model tractor
simulated tractor driver
(a raw egg)
ROPS
steering
wheel

## Slide 8: Why fasten the seat belt?
A seat belt can be
the difference between life and death
x
x
ROPS
overturned model tractor
crushed simulated
tractor driver

## Slide 9: Effectiveness of ROPS & seat belts
In this case, the ROPS saved his life. A
buckled seat belt would have saved his legs,
prevented huge medical bills, and a permanent disability.
A ROPS alone greatly reduces the risk of being
killed during an overturn compared to a tractor
without a ROPS. Add a fastened seat belt and the operator is usually not injured in an overturn.
ROPS
Together ROPS and fastened seat belts are 98% effective in preventing injury and death during tractor overturns.

## Slide 10
How many people are in this picture?
A tough quiz!
What happened to these farmers?

## Slide 11
How many would have survived with a ROPS and seat belt?
All 108. Don't become a grim statistic. Get a ROPS and buckle up!
These 76 Kentucky farmers died in tractor overturns in 1994-99.
Another 32 farmers died when they fell off moving tractors.
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP
RIP

## Slide 12: ROPS & seat belts could have saved 108 lives*
Tractor overturns 76
Thrown from tractor and run over 25
Thrown from tractor but not run over 7
Highway motor vehicle & tractor collisions** 2
Total deaths 110
Potential lives saved by ROPS & seat belts 108
*KY Fatality Assessment and Control Evaluation (FACE) data 1994-99.
** These two collisions involved large vehicles traveling at high speed. ROPS and seat belts might not have prevented these two deaths.

## Slide 13: Kentucky farmers at risk-1996
In 1996, the KY fatality rate in Ag/Forestry/Fishing was 2.8 times the national rate.
In KY, nearly all of these deaths were farming related.

## Slide 14: Tractor-related farm deaths
Average for US
Farming States
National Safety Council
1998 data for the US
Kentucky 1994-98
UK Kentucky Fatality Assessment
and Control Evaluation data

## Slide 15: Lifetime chance of an overturn
1 in 9 Kentucky farmers age 55 or older have overturned a tractor and lived
1/3 of these survivors have had two or more overturns
many of these persons were injured
  some received minor injuries
  some received severe injuries
  some were permanently disabled

## Slide 16: Use of ROPS on Kentucky farms

## Slide 17: Of 100 Kentucky farmers who drive tractors
only 6 are fully protected by ROPS and seat belts

## Slide 18
another 24 farmers who drive tractors with ROPS
don’t wear their seat belts
another 24 farmers who drive tractors with ROPS
don’t wear their seat belts

## Slide 19
another 70 farmers are unprotected because they
drive tractors without ROPS and seat belts
Risky business!