## Slide 1
NICEATM ICCVAM
National Toxicology Program Interagency Interagency Coordinating Committee Center for the Evaluation Of Alternative on the Validation of Alternative Toxicological Methods Methods
The Bovine Corneal Opacity
and Permeability (BCOP)
Test Method
BRD Summary
Expert Panel Meeting
January 11-12, 2005
Bethesda, Maryland

## Slide 2: Current U.S. Regulatory Status of BCOP
ICCVAM agencies were surveyed
BCOP data was submitted to EPA and FDA for consideration

## Slide 3: Primary BCOP Data Sources
Study | Accuracy (S/NS) |  |  | Intralab (S/NS) | Interlab (S/NS) | 
 | GHS | EPA | EU | CVs | CVs | GHS class.
Gautheron et al. (1994) | 7/6 | 6/6 | 8/43 | - | 52 | 7/6
Balls et al. (1995) | 22/35 | 20/35 | 21/38 | - | 59 | 22/35
Swanson et al. (1995) | 6/3 | 6/3 | 5/4 | 20a | - | -
Gettings et al. (1996) | 8/17 | 10/15 | 6/19 | 25b | - | -
Casterton et al. (1996) | 26/30 | 26/29 | 24/36 | - | - | -
Southee (1998) | 6/8 | 6/8 | 5/10 | 16c | 16 | 6/8
Swanson and Harbell (2000) | 1/8 | 4/5 | 1/8 | - | - | -
Bailey et al. (2004) | 3/13 | 3/13 | 3/13 | - | - | -
Dr. Joseph Sina’s submission | - | - | - | 29d | - | -
S = severe or corrosive irritants; NS = nonsevere irritants or nonirritants; class. = classification.
a Intralaboratory repeatability was evaluated (n=5 corneas). Data received after publication of draft BRD. b Intralaboratory reproducibility was evaluated (n=3 replicate experiments). cIntralaboratory repeatability and reproducibility were evaluated. d Intralaboratory repeatability was evaluated (n=4 corneas).
*In vivo data not available for this study.

## Slide 4: Other BCOP Reports Considered
31 other reports were identified that could not be used for an evaluation of accuracy or reliability due to the lack of:
  appropriate comparative in vivo rabbit test data (i.e., raw scores for individual animals)
  quantitative in vitro data
  adequate information on test substances
  in vivo data obtained from currently accepted regulatory test guidelines
These reports discussed in Section 9
To the extent possible, data requested from authors of studies considered most useful

## Slide 5: Database
166 different substances or formulations evaluated
15 Chemical classes tested*
  Most frequent classes: formulations, alcohols, heterocyclic compounds, acids and ketones
20 Product classes tested*
  Most frequent classes: solvents, chemical/synthetic intermediates, drugs/pharmaceuticals, petroleum products, cleaners, personal care cleansers, and hair shampoos
*Classes with at least 3 entries

## Slide 6: Test Method Protocol Variations
BCOP test method protocols were similar to each other, but not identical
Examples of test method components that differed among protocols used to generate data include:
  Storage conditions of bovine eyes during transport (e.g., use of antibiotics, ambient temperature vs. over ice)
  Use of MEM with or without phenol red for incubations
  Instrument used to measure opacity (opacitometer vs. spectrophotometer)
  Use of positive controls
  Use of different negative controls (e.g., saline vs. sterile deionized water)
  Application of solid test substances (20% suspension vs. neat substance)
  Analysis of resulting data
  Addition of other endpoints, such as histology

## Slide 7: BCOP Data Analysis Methods
In Vitro Irritancy Score (IVIS)*
  IVIS = mean opacity value + (15 x mean OD490 value)
  IVIS > 55.1 = severe irritant
Endpoint with highest score**
  Permeability > 0.600 = severe irritant
  Opacity > 1.300 = severe irritant
Permeability value only
  Some studies analyzed permeability data only for substances that produce significant permeability without appreciable opacity
    anionic and nonionic surfactants
    some surfactant-based personal care formulations
Comparison to benchmark substances
*Used in protocols that measure opacity with an opacitometer.
**Used in protocols that measure opacity with a UV/VIS spectrophotometer.

## Slide 8: Distribution of Tests Among Analysis Methods*
Method | Number of Testing Laboratories |  |  | 
 | 1 | 3 | 5 | 11/12
In Vitro Irritancy Score | 28 | 16 | 51 | 52
Opacity or Permeability | 60 |  |  | 
Permeability only | 25 |  |  | 
Comparison to benchmark | 9 |  |  | 
*Includes only tests for which in vivo data were available.

## Slide 9: BCOP Accuracy Analysis
Ability of analysis methods to correctly identify ocular corrosives and severe irritants determined for
  GHS classification system (Category 1)
  EPA classification system (Category I)
  EU classification system (R41)
Accuracy statistics calculated for:
  each BCOP study with in vitro and in vivo data
    by test substance
    by test
  pooled data from studies with similar protocols
False negative and false positive rates calculated by chemical class and available physicochemical properties (liquid/solid)

## Slide 10: Overall BCOP Accuracy Results*
*BCOP data from the the following studies were pooled for this analysis: Gautheron et al. (1994), Balls et al. (1995), Swanson et al. (1995), Gettings et al. (1996), Swanson & Harbell (2000), Bailey et al. (2004).
**Additional 37 chemicals available for EU analysis only (individual animal data not available for GHS or EU classification)
Statistic | GHS (n=120)* |  | EPA (n=117)* |  | EU (n=157)** | 
 | % | n | % | n | % | n
Accuracy | 79 | 95/120 | 80 | 93/117 | 77 | 121/157
Sensitivity | 76 | 32/42 | 73 | 33/45 | 77.5 | 31/40
Specificity | 81 | 63/78 | 83 | 60/72 | 77 | 90/117
False Positive Rate | 19 | 15/78 | 17 | 12/72 | 23 | 27/117
False Negative Rate | 24 | 10/42 | 27 | 12/45 | 22.5 | 9/40

## Slide 11: BCOP False Negative & False Positive Rates by Chemical/Physical Class (GHS)
Category | n | False Negative Rate |  | False Positive Rate | 
 |  | % | No. | % | No.
OVERALL | 120 | 24 | 10/42 | 19 | 15/78
Formulations with surfactants | 34 | 14 | 2/14 | 5 | 1/20
Alcohol | 10 | 100 | 1/1 | 44 | 4/9
Formulation, ethanol containing | 8 | 0 | 0/1 | 29 | 2/7
Surfactant, cationic | 7 | 0 | 0/6 | 0 | 0/1
Acetate | 6 | - | - | 0 | 0/6
Formulation, petrochemical | 6 | 33 | 1/3 | 0 | 0/3
Acid | 5 | 0 | 0/3 | 50 | 1/2
Heterocyclic compound | 5 | 25 | 1/4 | 0 | 0/1
Surfactant, nonionic | 4 | - | - | 50 | 2/4
Aromatic hydrocarbon | 3 | - | - | 0 | 0/3
Inorganic chemical | 3 | 50 | 1/2 | 0 | 0/1
Ketone | 3 | - | - | 67 | 2/3
Alkali | 2 | 0 | 0/1 | 100 | 1/1
Amine; Cyclic Hydrocarbon; Oil | 2 | - | - | 0 | 0/2

## Slide 12: BCOP False Negative & False Positive Rates by Chemical/Physical Class (con’t)
Category | n | False Negative Rate |  | False Positive Rate | 
 |  | % | No. | % | No.
Petrochemical, cutting fluid | 2 | - | - | 0 | 0/2
Polycyclic aromatic hydrocarbon | 2 | 0 | 0/2 | - | -
Surfactant, anionic | 2 | 100 | 1/1 | 0 | 0/1
Acyl halide; Amide | 1 | - | - | 0 | 0/1
Aldehyde; Organophosphate | 1 | - | - | 100 | 1/1
Amidine | 1 | 0 | 0/1 | - | -
Chlorinated hydrocarbon; Lactone | 1 | - | - | 0 | 0/1
Diol |  | 100 | 1/1 | - | -
Organometallic | 1 | - | - | 0 | 0/1
Organophosphate | 1 | - | - | 100 | 1/1
Quaternary ammonium surfactant | 1 | 100 | 1/1 | - | -
Terpene; Wax | 1 | - | - | 0 | 0/1
Thiophthalimide | 1 | 100 | 1/1 | - | 1
Liquid | 94 | 18 | 5/28 | 21 | 14/66
Solid | 19 | 33 | 4/12 | 29 | 2/7

## Slide 13: Limitations of BCOP Accuracy Analysis
For a majority of the chemical classes (63%; 20/32), only a small number (≤2) of substances were tested
Only 6 chemical classes for which ≥5 substances were evaluated in BCOP
Limited information about physicochemical (e.g., solid, liquid) properties for some test substances
A few substances were tested in multiple in vivo studies that produced different in vivo classifications; the most severe classification was used for the analysis
Individual rabbit eye data not available for Gautheron 1994 interlaboratory study at time of draft BRD publication; data just received, which will provide additional information for GHS and EPA accuracy analyses

## Slide 14: BCOP Reliability Analysis
Intralaboratory Repeatability and Reproducibility
  Quantitative analysis: Coefficient of variation
Interlaboratory Reproducibility
  Qualitative analysis: Extent of agreement between testing laboratories when identifying corrosives and severe irritants
  Quantitative analysis: Coefficient of variation

## Slide 15: BCOP Intralaboratory Repeatability - %CV Values for In Vitro Irritancy Score
 | %CV | Dr. Sina Submission | Swanson et al. 1995* | Southee 1998 (Lab 1) | Southee 1998 (Lab 2) | Southee 1998 (Lab 3)
All Data | Mean | 71 | -44 | 48.3 | 39.2 | 30.5
 | Median | 35 | 7.9 | 14.2 | 11.8 | 12.4
 | Range | 1.1 - 479 | -782 - 32.5 | 0.1 - >500 | 2.1 - >500 | 4.3 - >500
Substances Predicted as Severe | Mean | 8.2 | Not calculated | 8.44 | 8.4 | 11.1
 | Median | 8.1 | Not calculated | 7.05 | 8.1 | 9.3
 | Range | 1.1 - 13 | Not calculated | 0.1 - 22 | 2.1 - 21.7 | 5.1 - 30.3
*Replicate cornea data received December 23, 2004

## Slide 16: BCOP Intralaboratory Reproducibility
Gettings et al. 1996: 25 substances, 3 trials, 1 lab
  Mean and Median %CV for permeability value was 33.4 and 29
  Substances spanned a range of irritancy
  Surfactant-based personal care cleaning formulations
Southee 1998: 16 substances, ≥ 2 trials, 3 labs
  Mean %CVs for IVIS ranged from 12.6 to 14.8 for the 3 labs
  Median %CVs for IVIS ranged from 6.7 to 12.4 for the 3 labs
  Substances spanned a range of irritancy

## Slide 17: BCOP Interlaboratory Reproducibility - Classification Agreement Among Laboratories
% Interlab Agreement | Balls et al. 1995 (5 labs): GHS |  | Southee 1998 (3 labs): GHS |  | Gautheron et al. 1994 (11 or 12 labs) | 
 | % | N | % | N | % | N
100% (all) | 68 | 41/60 | 94 | 15/16 | 71% | 36/51
80% (all) | 85 | 51/60 | 94 | 15/16 | 91 | 46/51
100% (severe in vivo and in vitro) | 82 | 14/17 | 100 | 3/3 | 60 | 3/5
80% (severe in vivo and in vitro) | 94 | 16/17 | - | - | 80 | 4/5

## Slide 18: BCOP Interlaboratory %CV Values for In Vitro Irritancy Score
 | %CV | Gautheron et al. 1994 (11 or 12 labs) | Balls et al. 1995 (5 labs) | Southee 1998 (3 labs)
All Data | Mean | 168 (n=52) | 50 (n=50) | 32 (n=16)
 | Median | 46.9 (n=52) | 26 (n=50) | 23 (n=16)
 | Range | 16.5 - 1325 (n=52) | 7.6 - 712 (n=50) | 7.5 - 109 (n=16)
Substances Predicted as Severe | Mean | 36 (n=17) | 25 (n=32) | 11.1 (n=5)
 | Median | 17 (n=17) | 22 (n=32) | 8.6 (n=5)
 | Range | 16.5 - 55.7 (n=17) | 7.6 - 89.4 (n=32) | 7.5 - 21.6 (n=5)

## Slide 19: Limitations of BCOP Reliability Analysis
No major limitations identified

## Slide 20: Draft BCOP BRD Proposals (1)
A recommended BCOP version identified, which evaluates
  Opacity and permeability
  Histology recommended on a case-by-case basis (see Section 2.2.3 of BRD; Appendix A-22)
A standardized protocol proposed for the recommended version of the BCOP test method
  Protocol based on the method used by the Institute for In Vitro Sciences (IIVS)
  Only significant difference is that the recommended protocol in the BRD lacks the detailed histology procedures provided in a separate IIVS protocol on histology for the BCOP assay
  Decision criteria previously described by Gautheron et al. (1994)

## Slide 21: Draft BCOP BRD Proposals (2)
Proposed optimization studies recommended, including:
  Retrospective analysis of decision criteria used to identify corrosives and severe irritants
  An evaluation of possible increased interlaboratory variability for specific chemical classes appearing more variable (e.g., alcohols)
  An evaluation of reduced exposure times for alcohols, and possibly other volatile solvents
  Determining the utility of histopathology and when it should be included.
Once optimized, additional validation studies recommended to further assess the accuracy and reliability of BCOP, so that the applicability domain can be better defined and data gaps can be filled in