## Slide 1: Halon Replacement Lavex Bottle Tests
Richard J. Mazzone
Payloads Design
Boeing Commercial Airplane Group
March 27 & 28, 2001

## Slide 2: Lavatory Trash Container Fire Extinguisher (Lavex) Test
Status
Boeing requested all interested suppliers to submit data to show they have an agent/bottle candidate that meets Spec 10-61909.
Reviewed supplier drawings & data & authorized five suppliers to proceed to alternative agent screening test at FAA Tech Center
Requested seven non-Halon and three Halon bottles from each supplier.
    (FAA conformity of non-Halon bottles done per
    supplier drawing w/exception noted)
Requested two more Halon bottles from two different suppliers to re-validate test equipment and data collection system.
Tested three agents from four suppliers week of Dec 11, 2000.

## Slide 3: Lavatory Trash Container Fire Extinguisher (Lavex) Test
Results
Two agents passed
    FM-200™ (HFC-227ea) one supplier
    FE-36™ (HFC-236fa) two suppliers
One agent from one supplier failed
    Envirogel™ (Ammonium Polyphosphate in HFC 134a)
    Failure analysis being performed by supplier

## Slide 4: FAA Test Setup

## Slide 5: Lavatory Trash Container Fire Extinguisher (Lavex) Test
Lessons Learned
Obtain concurrence on Test Acceptance Criteria before test starts
    Suppliers, TBC & FAA Airworthiness Certification Office
Test box leaked at air supply shut off slider
    Discovery/repairs made early in tests
Revision to MPS to clarify Appendix D
    Revise wording of discharge performance criteria (Sec. 4.5)
    Add location of upper thermocouple (Sec 5.2.3)
    Add upper thermocouple to Figure D-1. (page D-9)
Data gathering interval should be less than five seconds apart

## Slide 6: Lavatory Trash Container Fire Extinguisher (Lavex) Test
Next Steps
Successful suppliers preparing to submit Qualification Test Procedure to Boeing for review
Suppliers then perform Qual tests with FAA conformed bottles
Bottle passing Qual tests will then be tested by Boeing in actual waste compartment installation using conformed bottles
Boeing Lavatory specification will be revised to add suppliers part number for bottles that meet all requirements
Lav suppliers are then authorized add those parts to their own drawings