## Slide 1
Long Term Biological Monitoring on the Upper Mississippi River:
A Springboard For Broad-Scale, Multidisciplinary Investigations
David M. Soballe
U.S. Geological Survey
Upper Midwest Environmental Sciences Center

## Slide 2
LTRMP
NASQAN
NAWQA
USEPA
USACOE
NRP
Districts
USFWS
NPS
USDA
INHS
IEPA
WDNR
MPCA
IDNR
MoDC
MDNR
Met.Council
UMR PARTNERS
UMESC

## Slide 3
UMESC
LTRMP
Provides Foundation and Connecting Web for Big River Ecological Studies
UMR PARTNERS

## Slide 4: LTRMP Part of the Environmental Management Program (EMP)
Established by Act of Congress in 1986 to counter effects of navigation
2/3 EMP budget = Habitat Rehabilitation and Enhancement Program (HREP -USACOE)
1/3 EMP budget = Long Term Resource Monitoring Program (LTRMP-USDOI)
USACOE given oversight responsibility

## Slide 5
LTRMP Study Area: The Upper Mississippi River System (UMRS).
Mississippi River mainstem between Ohio River and St. Paul, Minnesota, plus the Illinois River

## Slide 6: The LTRMP is Multi-Disciplinary: Research, Monitoring, and Data Access
Fisheries
Water Quality
Aquatic and Floodplain Vegetation
Aquatic Invertebrates
Sedimentation and Bathymetry
Land Cover and Land Use
Data Delivery

## Slide 7: LTRMP WQ Activity Driven by Resource Management
Detect changes in habitat availability and suitability
Assess normal variations and natural interactions among river biota and the physiochemical environment
Evaluate effects of human activities
Evaluate effects of watershed inputs
Link river biology to transport and transformation of nutrients and sediment

## Slide 8: Upper Mississippi Resource Issues Cover a Broad Spectrum
nutrients
aquatic habitat
sedimentation
navigation
water supply
waste disposal
flood control
hydropower
recreation
water quality
toxic spills
migratory animals
hypoxia
sustainable agriculture
buffer zones
contaminants
biotic diversity
endangered species
native cultures
history & archaeology
Notes: Add slides from Hank showing basin landcover and nutrient applications.

## Slide 9: Two-Phase Approach to Limnological (WQ) Monitoring in LTRMP
Fixed site sampling (FSS) at permanent locations and fixed intervals (2- 4 weeks)
Stratified random sampling (SRS) conducted quarterly
Notes: Add slides from Hank showing basin landcover and nutrient applications.

## Slide 10: Fixed Locations - Fixed Intervals
Permanent sampling locations (8-20) in each of 6 study reaches
Focus on short-term variations, watershed influences, downstream transformation and transport
2 - 4 week sampling intervals
About 3,800 site visits per year
Notes: Add slides from Hank showing basin landcover and nutrient applications.

## Slide 11: Stratified Random Sampling
Gives unbiased estimates of seasonal conditions in broad aquatic areas within the study reaches
Quarterly sampling in specific date windows
2-5 sampling strata (probability sample) in each of 6 study reaches
150 sites per episode, per study reach (3,600 site visits per year)
Notes: Add slides from Hank showing basin landcover and nutrient applications.

## Slide 12
SRS Spatial Scale

## Slide 13: Water Quality Measurements
Total nitrogen
Ammonium
Nitrate + nitrite
Total phosphorus
Soluble reactive phos.
Dissolved Silica
Total suspended solids
Volatile suspended solids
Chlorophyll/phytoplankton
Ions : Ca,K,Mg,Na: Cl,SO4
Sediment
Water depth
Secchi transparency
Ice and snow
Temperature
Dissolved oxygen
pH
Conductivity
Turbidity
Velocity
Notes: Add slides from Hank showing basin landcover and nutrient applications.

## Slide 14: LTRMP WQ Provides Fundamental Limnological Information
Emphasis on biological aspects of water quality: nutrients, sediment, and physical limnology
1993 to present: 7 study reaches (9 navigational pools, 40 tributaries)
Only source of current limnological data for much of Upper Mississippi River System

## Slide 15: Program Resources Are Stretched
Over 1,000 river miles within the study area
  Six field stations with staff
  About $150 per site visit
85,000 chemical measurements in 1999
  Lab & Field QA/QC = about 40% of total
  about $2.50 per measurement (12% of WQ budget in LTRMP)
30% reduction in effort in FY2000
  additional reductions likely.
Notes: Add slides from Hank showing basin landcover and nutrient applications.

## Slide 16: LTRMP Supports Multiple Scales of Investigation and Collaboration
Whole Basin - Decades
River reaches (multiple years)
Individual locations (hours-years)
Notes: Add slides from Hank showing basin landcover and nutrient applications.

## Slide 18
Fall Nitrate + Nitrite in Pools 4, 8, and 13

## Slide 19: Total Nitrogen Flux in Pool 13
Input
Output
Notes: Spatial Patterns from Hank
Long-term patterns:
Alton, Keokuk, Winona.Clinton.
Delivery ratios for these subbasins.

## Slide 20
Mississippi River near Harper’s Ferry, Iowa (Pool 10)

## Slide 21
OK
unsuitable

## Slide 22: UMR Collaborations Within USGS Are Well Established
LTRMP-UMESC-NRP
UMESC-LTRMP
LTRMP – NASQAN
LTRMP-Districts-NASQAN
Notes: Add slides from Hank showing basin landcover and nutrient applications.

## Slide 23: LTRMP And NASQAN?
Differing objectives, differing design, but overlap in study areas and parameters
Collaborations in selected areas seem very promising
A more complete picture can be obtained in combination than in isolation
Notes: Add slides from Hank showing basin landcover and nutrient applications.

## Slide 24: Differing Focus = Differing Design
NASQAN:
  Rating Curve approach
  Long-term flux of many parameters
  Broad spatial scale
LTRMP:
  Habitat and long-term biotic response in UMR
  Short-term, spatially-varying events
Notes: Add slides from Hank showing basin landcover and nutrient applications.

## Slide 25: Design Differences
NASQAN
  Infrequent (monthly, quarterly)
  Integrated, isokinetic channel cross-sections
  Many parameters
  Few locations (3-4 in UMR)
LTRMP
  Frequent (biweekly, monthly, quarterly)
  Discrete horizontal & vertical samples
  Few transects, few vertical profiles
  Fewer parameters
  Many locations (about 1000)
Notes: Add slides from Hank showing basin landcover and nutrient applications.

## Slide 26: Common Locations
Clinton
Grafton
Thebes
Notes: Add slides from Hank showing basin landcover and nutrient applications.

## Slide 27: Comparability of Flux at Thebes
Suspended Solids
Total Phosphorus
Notes: Add slides from Hank showing basin landcover and nutrient applications.

## Slide 28: Short-term Patterns Not Addressed by NASQAN
Notes: Add slides from Hank showing basin landcover and nutrient applications.

## Slide 29: Additional NASQAN-LTRMP Comparison and Collaboration Underway
Splitting samples between labs
Simultaneous sampling
Comparisons of existing data at Thebes, Grafton, and Clinton are progressing
Modelling to better cross-calibrate
Notes: Add slides from Hank showing basin landcover and nutrient applications.

## Slide 30: EXAMPLE II: The Flood of 2001
Combined BRD/WRD investigation
In-place capabilities allow this event to be monitored.
Combining expertise and sampling networks across divisions gives a more complete view.
See Poster
Notes: Add slides from Hank showing basin landcover and nutrient applications.

## Slide 31: Combined Contributions
WRD and NASQAN: discharge records, lower Miss. and Ohio concentrations
WRD Iowa City: special flood monitoring, (Lagrangian) of concentrations.
BRD and LTRMP: flood concentrations by routine monitoring.
BRD and WRD – data analysis and interpretation, joint authorship of manuscript.
Notes: Add slides from Hank showing basin landcover and nutrient applications.

## Slide 32: Preliminary Results
Spring flood (2001) substantially different from Spring-Summer Flood (1993)
Flood from uppermost basin (2001) unlike flood of entire region (1993).
2001 flood volume was unremarkable below Thebes, but [NOx] was near records.
Lack of dilution from lower basin (Ohio) in 2001 sent high [NOx ] to the Gulf.
Notes: Add slides from Hank showing basin landcover and nutrient applications.

## Slide 33
WWW.UMESC.USGS.GOV
Thanks,
Dave Soballe & Dennis Wasley

## Slide 36: Primary LTRMP Products
Unique information for resource managers and decision makers on large rivers
High-quality, relevant data, in readily accessible and useable forms
Notes: Add slides from Hank showing basin landcover and nutrient applications.

## Slide 37: Common Ground
Overlap in major water quality constituents measured.
Both address long-term temporal patterns in the Upper Mississippi River.
Data collected at overlapping locations.
Comparable measurements obtained to the extent allowed by differing objectives.
Notes: Add slides from Hank showing basin landcover and nutrient applications.