## Slide 1: The NASA STEP Testbed Pan Galactic Engineering Framework (PGEF) Implementing a STEP-based Intelligent Master Model for Systems Engineering and the “Model-Based Enterprise”
Stephen C. Waterbury
NASA / Goddard Space Flight Center
April 8, 2003
Aerospace PDE 2003 Workshop
at NIST
Notes: NASA’s Intelligent Synthesis Environment (ISE) initiative and its Collaborative Engineering Environment (CEE) will require sophisticated capabilities for the sharing and configuration management of engineering models. Engineers using these advanced environments will have state-of-the-art tools for Computer-Aided Design, Analysis, Simulation, Systems Engineering, Software Engineering, and other engineering disciplines. Each of these discipline’s tools focuses on a view that is in some ways unique and separate from other engineering disciplines, and yet the design of a particular item often requires a collaboration between two or more disciplines -- for example, a printed circuit assembly must be designed and analyzed from the mechanical as well as the electrical point of view in order to meet all system requirements.
The engineering models on which the tools of different disciplines operate are unique in important ways, but if tools from different disciplines are brought to bear on a single product, it is important for data integrity that all tools work to a common underlying structure. This common underlying structure is contained in the STEP standard (ISO 10303), “STandard for the Exchange of Product model data”.
This presentation will discuss how STEP can be used to provide a common structure to which all engineering discipline models refer, so that data integrity and configuration management are maintained.

## Slide 2: PGEF Acronyms and Definitions
API ……….... Application Programming Interface
CAD ……….. Computer-Aided Design
CAE ……….. Computer-Aided Engineering (typically, analysis)
Express …... an information modeling language
Express-X … maps between & creates views of Express models
PDM ……….. Product Data Management
PGEFTM ……. Pan Galactic Engineering Framework
PGPDM …… Pan Galactic PDM (a PGEF application)
SE ................ Systems Engineering
STEP ………. Standard for the Exchange of Product Model Data (ISO 10303)

## Slide 3: The NASA STEP Testbed
Purpose: Leverage STEP technology to support collaborative engineering in NASA projects
Approach: Implement STEP-based software for Systems Engineering (SE) and Model-Based Enterprise (MBE)
  Pan Galactic Engineering Framework (PGEF) software
  NASA federated STEP-based Systems Engineering Repository
  Collaborate with and support NASA centers in implementation and deployment

## Slide 4: Goals of PGEF (Hub or “Server” Functions)
Integration of model information from all engineering disciplines (electrical, mechanical, analysis, systems engineering, etc.)
Standards-based Dictionary service for import and management of data dictionaries
Unified view of all system modeling parameters (which are referenced in the data dictionary!) throughout the life cycle
Management of Structured Product Documents* linked to CAX/SE models
Standard model library and archive, enabling design re-use
Support for “model-driven” acquisition (model-based specs, etc.)
Full spectrum of model repository services, including CM and long-term data retention (archiving)
* Structured Product Documents: documents of which some portion is linked to (and should be validated against) product data. Examples: Requirements, ICD, Drawings, ECR, ECO, Specifications

## Slide 5: Goals of PGEF (UI or “Client” Functions)
Product Data Browser (analogous to Web browser)
Searching and browsing model information from all engineering disciplines (electrical, mechanical, analysis, systems engineering, etc.)
Dictionary terms search, browsing, creation, and editing
Model parameter reporting, inspection, notification (by several methods) of changes or impacts, and display of applicable dictionary definitions
Creation and editing of Structured Product Documents*, validated against applicable models and dictionaries in the repository
User and tool interfaces to model libraries and archives
Creation of various types of conceptual, functional, behavioral, and physical assembly trees for trade studies, digital mock-ups, and simulations
* Structured Product Documents: documents of which some portion is linked to (and should be validated against) product data. Examples: Requirements, ICD, Drawings, ECR, ECO, Specifications

## Slide 6: Okay, fine, but why Python?!
Very coherent language and library structure
  Deeply Object Oriented (built-in types are objects, too – strings, etc.)
Clear syntax – makes for code that’s easy to understand and maintain
  Almost “pseudo-code”
  Excellent automatic documentation generators
Platform-independent
  Possibly even more so than certain other languages that claim to be … ;^)
  Only one implementation of Python interpreter on each platform
Plays well with other languages and on various platforms, so is an excellent integration language
  Extensible with C or C++
  Has COM, CORBA, various other libraries
  Is used by Google, Pixar, Verity, and others for this purpose
Other cool stuff …

## Slide 7
Model-Based Enterprise Master Model Integration Using STEP
AP 233
AP 210
AP 209
AP 203
Analysis (CAE)
Tools
Electronic CAD
Tools
Systems Engineering
Tools
Mechanical CAD
Tools
Spacecraft X
Master Model
Integrated STEP
Master Model
Express-X
Maps
Instrument Y
Master Model
Pan
Galactic Client
Instrument Y
Object
Notes: This diagram illustrates the concept of “Intelligent PDM”. The essential ingredients for Intelligent PDM are:
  (1) a set of discipline-specific information models (the examples shown are the STEP Application Protocols 203 [MCAD], 209 [Finite-Element Analysis], 210 [ECAD], and 232 [Systems Engineering]);
  (2) STEP translators for the discipline tools: since Intelligent PDM is based on STEP, each tool to participate in this environment must have a STEP import/export capability;
  (3) a Product Master Model, which incorporates the STEP AP’s as subsets and represents each common object once. For example, the geometry of the product is a subset of the Product Master Model, and is “reflected” in the MCAD, ECAD, and Analysis models, in which it may have different projections (e.g., 2-D or “2.5”-D in an ECAD model) or transformations to lower fidelity. The Product Master Model could be thought of as a “union” or “superset” of all the discipline models of the product.
  (4) mappings between the discipline-specific views of the product (the STEP AP’s) and the Product Master Model. These mappings are being developed using the EXPRESS-X mapping language, a new part of the STEP standard.
The diagram depicts the discipline tools feeding their models through the STEP AP’s and mappings into the Master Models for Spacecraft X and Instrument Y. The Intelligent PDM system can then generate, through the reverse mappings, the changed versions of the other discipline models.

## Slide 8: The Product Master Model Evolution Population of Master Model Contents Over the Project Life Cycle
Requirements
Functional Model
Mission Parameters
Preliminary Components
Requirements
Functional Design
Behavioral Model
Mission Parameters
Physical Model
Pre-Phase A
Integrated Mission Proposal
Phase A/B
Prototyping and Analysis
Phase C/D
Detailed Design, Build, and Test
Requirements
Functional Design
Behavioral Design
Physical Design/Arch.
Interface Control Docs
Mission Parameters
Notes: Another benefit of the Intelligent PDM approach is that it provides continuity of the product’s definition as it evolves through the various phases of its development life cycle.
Imagine the Product Master Model’s framework as a large set of “shelves” or labeled compartments for the various aspects of a comprehensive product model. In the early conceptual definition of the product (corresponding to Pre-Phase A studies for a NASA mission), only a few of the shelves or compartments are populated, and that data may not be complete in the early stages. Still, it is important to propagate that high-level data, containing requirements and mission parameters, to the later phases of development and to allocate it to the various aspects of system design that it defines and constrains. These allocation relationships are supported in the Product Master Model, and can be viewed by the systems engineer at any point by extracting the systems engineering view of the evolving Master Model.
In the early phases, the model may be populated just enough to enable low-fidelity simulations, for example. Another benefit of the Product Master Model is the capability to identify what additional data is needed in order to generate particular types of analysis or simulation models.
As the Product Master Model becomes fully populated, more detailed views and simulation models can be generated, until finally the design model can be used to generate detailed drawings and fabrication models.

## Slide 9
File Vault
(STEP, XML, PDF, proprietary, etc)
Database:
PostgreSQL
Security, Auth., and Request
Routing
Services: Twisted
Transaction
and Repository
Manager:
PGER (DB-API,
O-R Mapping,
Object Model Customization)
Model
Validation and Transformation Services: Express Engine
(Express-X Views and Maps)
“Thick”
Client
API:
Twisted (XML-RPC, SOAP, CORBA, PB, etc)
UI Module
Components:
Structure Trees, Grids,
Wizards/Editors, Local OODB, Interfaces (e.g. COM, XMLRPC),
Protocols
(e.g. HTTP, IIOP, Perspective Broker, etc)
System
API:
(peer/peer, federation, hub services)
“Thin” Client API:
Web
Web Browsers
External Systems
(PDM, etc.)
CAD/CAE, Desktop Tools

## Slide 10
PGER
Express
Engine
File Vault/Storage
(Unix Filesystem)
PostgreSQL
Check-in Process
1. File upload
2. RM calls Expresso to run Express-X to extract PDM data.
3. Expresso outputs XML-encoded
PDM data.
4. RM executes transaction to write
mapped data into PostgreSQL and AP210 file to “vault” (mapped data contains a reference to the file).

## Slide 11: Use Cases
Collaborative High-Level Mission Analysis
  Participants: several users, at possibly distributed sites
  Roles: systems engineer, engineers in several different disciplines, principal investigator (scientist), [others?]
  Processes:
    Capture of initial mission parameters / requirements (via spreadsheet entry and/or other means) [--> further define what “capture” means, plus what are CM requirements for this process …]
    Proposal and analysis of alternate mission scenarios (including technologies, specific vehicles/components/etc.) and record each with comments, parameters, calculations, analyses, etc. [--> further define types of data to go into these mission scenario analysis “packages”]

## Slide 12: Use Cases
Distributed Multi-Disciplinary Simulations
  Participants: several users, at possibly distributed sites
  Roles: engineers in several different disciplines, systems engineers, engineering management, project management
  Processes:
    Level 1: Creation and CM of assembly trees of possibly multi-disciplinary simulation models, with model parameters coordinated among discipline models
    Level 2: HLA implementation; repository-driven “hub” services for distributed simulation with CM and histories
    Levels 3-n TBD (further integration with design and analysis models and modeling processes, etc.)

## Slide 13: Use Cases
Collaborative Multi-Disciplinary Design and Analysis
  Participants: several users, at possibly distributed sites
  Roles: engineers (designers/analysts) in several different disciplines, [systems engineer,] [project management,] [others?]
  Processes:
    Level 1: Capture and CM of design and analysis models, documents, comments, etc. (essentially, basic PDM)
    Level 2: Sharing of geometries and semantics between discipline models (ex.: Electromechanical scenario: “round-trip” model exchanges between disciplines)
    Level 3: Derivation of analysis models from design models (ex.: Russell Peak’s “PBAM” concept) [--> this scenario has many levels and possible modes of implementation]
    Levels 4-n TBD (simulations, optimizations, etc., etc.)

## Slide 14: Use Cases
Structured Product Document (SPD) Management
  Participants: several users, at possibly distributed sites
  Roles: engineers in several different disciplines, engineering management, project management, acquisition management
  Processes:
    Level 1: Creation, validation, CM, approval, and release/publishing of SPD’s, including full workflow, event notification, digital sign-off, and repository/Web access
    Level 2: Extensive use of Document Type Definitions (DTD’s), templates, and reusable doc components
    Level 3: Interactive interfaces with model CM process; SPD updating automated and user-monitored
    Levels 4-n TBD (full integration with modeling process, etc.)