## Slide 1: CALPUFF: Updates, Applications, and Recommendations
Eighth Modeling Conference Research Triangle Park, NC

## Slide 2: CALPUFF Workgroup
Mark Evangelista, NOAA/EPA
Desmond Bailey, NOAA/EPA
Dennis Atkinson, NOAA/EPA
Warren Peters, EPA.OAQPS
Peter Eckhoff, EPA.OAQPS
Herman Wong, EPA.R10
Kevin Golden, EPA.R8
Bret Anderson, EPA.R7
Al Cimorelli, EPA.R3
Clint Bowman, Univ.of Washington
Chuck Machovec, Colorado
Chris Arrington, West Virginia
Ken McBee, Virginia
Richard Fisher, USFS
John Notar, NPS
Tim Allen, FWS

## Slide 3: Workgroup Tasks
Identify the (technical) issues (Oct05)
Set recommendations, if possible
  If not, set up investigation of issue (Dec05)
Conduct coordination and review (Jan06)
Hold a workshop (Feb06)
Finalize recommendation report (Feb/Mar06)

## Slide 4: Interagency Workgroup on Air Quality Modeling
Coordinates among EPA and FLMs on long-range transport modeling for AQRVs.
  EPA (HQ and RO)
  NOAA (technical)
  USFS
  NPS
  FWS

## Slide 5: IWAQM History
IWAQM I
  Off-the-shelf for interim solution
  Limited, but better than nothing
IWAQM II
  Recommend the best modeling techniques or combinations of techniques.
  Recommendations become default settings and values

## Slide 6: IWAQM History
Presented at 6th Modeling Conference
  Endorsed use of mesoscale modeling with data assimilation
  Replaced MESOPUFF II with CALPUFF in IWAQM II.
  Recommended private/public committees to manage technical issues.

## Slide 7: IWAQM II Recommendations
Screening technique using CALPUFF
Include CALPUFF in Guideline on Air Quality Models
Long-range transport modeling for PSD
Modeling for visibility (AQRV)
Regional committees to manage decisions for PSD/AQRV modeling.

## Slide 8: CALPUFF Screening
Conservative determination of maximum concentration at any receptor for each distance.
In BART NPR modeling, used to populate lookup table
Less frequently performed as computational costs decline

## Slide 9: IWAQM Phase II Report…
“The control of CALMET options requires expert understanding of mesoscale and microscale meteorological effects and finesse to adjust the available processing controls within CALMET to develop the desired effects. The IWAQM does not anticipate a lessening in this required expertise in the future.”

## Slide 10: IWAQM Phase II Report…
“Appendix A provides a listing of the default settings recommended by IAWQM at this time. Some of these settings require testing, and we have attempted to note these. The information provided in Appendix A should not be interpreted as a cookbook approach to be applied, regardless of results obtained.”

## Slide 11: Meteorology
Expertise required – this won’t ever be as easy as ISC
  Mesoscale and microscale meteorology
Some met processors still need work
Particular formatting for met data
Recommendations are not cookbook

## Slide 12: Meteorology Example: Upper Air
If data gap is >12 hr, data must be filled by hand
  Using “expert judgment”
Operationally linked to
  FDDA in MM5(4)
  Data blending with CALMET

## Slide 13: Not Just Meteorological Expertise
Emissions
Geophysical characteristics
Receptor locating
Computational

## Slide 14: Geophysical Data
“Quality and uncertainties associated with long-range transport simulations is driven more by characteristics of the mixing depth and by the characterization of the transport winds.”
“The influence of local variations in land-use can be significant.”

## Slide 15: IWAQM Phase II “Requires”
Expert judgment
Site-specific decisions
Strong interaction and coordination with the applicable reviewing authorities
Consideration of computational expense and data size/access (FDDA studies)

## Slide 16: Visibility Example
Consult with experts
Run air quality model
Obtain background visibility
Obtain relative humidity adjustment factor
Determine Beta-extinction
Calculate delta-deciviews

## Slide 17: Where to Go from Here
CALPUFF evaluations
CALPUFF updates and improvements
Mechanism for adopting new version
Re-examination of recommendations
Mechanism for establishing new recommendations

## Slide 18: Evaluations, Updates… -- AQMG
Secondary formations
  SO2 to sulfate (gaseous) and NOx to nitrate (gaseous) are OK
  SO2 to sulfate (aqueous) not adequate
  Nitrate deposition (NH3 background?)
  For AQRVs, these processes are still better than assuming 0 secondaries (IWAQM II)

## Slide 19: Evaluations, Updates… -- AQMG
Downwind distance
  Puff coherency (shear splitting)
  Underestimates dispersion, over predicts concentration
  Horizontal: shear effects
  Vertical: change in mixing height at end of day

## Slide 20: Evaluations, Updates… -- AQMG
Ammonia limiting
PRIME downwash algorithm
Transitional plume rise
Rain caps and other horizontal releases
Wind convergence
PM2.5 transport

## Slide 21: CALPUFF Reviewer’s Guide (d)
Prepared by Air Resources Specialists for USDA Forest Service and National Park Service
Draft document
AQRV focus

## Slide 22: -- CALPUFF Reviewer’s Guide…
CALMET
  No Obs mode (NOOBS)
  Gridded clouds (ICLOUD)
  Kinematic effects (IKINE)
  Bias parameter (BIAS)
  Prog model in wind calc (IPROG)
  Radius of influence (NWS TD-3240 data)
  Lake breeze module

## Slide 23: -- CALPUFF Reviewer’s Guide…
RESTART
Final plume rise calculation (MTRANS)
Puff splitting (MSPLIT)
Dispersion coefficients (MDISP)
  Default is Pasquill-Gifford (#3)
  AERMOD micrometeorological method (#2)
    Recommended use along with probability density function for convection (MPDF)

## Slide 24: -- CALPUFF Reviewer’s Guide…
Regulatory default override off (MREG)
Subgrid scale complex terrain input (NHILL)
  Not used for long-range transport

## Slide 25: -- CALPUFF Reviewer’s Guide…
Deposition parameter settings
  Gaseous (dry) and particle (wet/dry)
Background concentrations
  Ozone
  Ammonia (land use weighted average)
Light extinction coefficients
F(RH) adjustment factors
Natural background conditions

## Slide 26: -- Comments on BART NPR…
MESOPUFF II and RIVAD chemistry is outdated
Aqueous chemistry is incorrect for sulfate formation
  Overestimates near sources
  Uncertain downwind
General over prediction beyond 200 km

## Slide 27: --Comments on BART NPR…
Nitrate and Sulfate formation rates are inaccurate
  Particularly nitrate in summer, sulfate in winter
  Model is highly sensitive to temperature effects
  Standard temperatures were assumed too high in chemistry
No accounting for NOX inhibiting photochemistry for sulfate formation

## Slide 28: Consultation with Other Modelers
Areas for evaluation
Recommendations needed
Future enhancements
A growing list – all input is welcome from modelers

## Slide 29: --Current Areas for Evaluation…
Use of “No Obs” Option
Turbulence Based Dispersion v. P-G Dispersion
Puff Splitting – Effective range of CALPUFF for modeling purposes
Light Extinction Calculation Methodologies

## Slide 30: --Current Areas for Evaluation…
Ammonia Limiting Method
CALPUFF Boundary Conditions
Aqueous Phase Chemistry
Secondary Organic Aerosols
Numerical plume rise algorithm (buoyant area and line sources)

## Slide 31: --Recommendations Needed…
“No Obs” – when are prognostic fields appropriate v. need for additional observations
  GAQM Section 9.3.1.2 (d) – “…mesoscale meteorological fields should be used in conjunction with available standard NWS or comparable meteorological observations within and near the modeling

## Slide 32: --Recommendations Needed…
Prognostic Meteorological Model Evaluation – statistical metrics and methodologies for determining acceptability of prognostic data sets.
  GAQM Section 9.3(c) – “Acceptance for use of output from prognostic mesoscale meteorological models is contingent upon concurrence by appropriate reviewing authorities that the data are of acceptable quality, which can be demonstrated through statistical comparisons with observations of winds aloft and at the surface at several appropriate locations.”

## Slide 33: --Possible Enhancements…
Chemistry Module Enhancements
  SCICHEM Aerosol Chemistry
  Aqueous Phase Chemistry
MCIP Style Processor for CALPUFF
  Bypass CALMET processing and rediagnosis of prognostic variables
  Direct use of prognostic meteorological data in CALPUFF

## Slide 34: Workgroup Tasks
Identify the (technical) issues (Oct05??)
Set recommendations, if possible
  If not, set up investigation of issue (Dec05??)
Conduct coordination and review (Jan06??)
Hold a workshop (Feb06??)
Finalize recommendation report (Feb/Mar06??)