## Slide 1: Pixel Clustering
Simplified presentation today ignores:
  Cross column clustering
  Magnetic field effects
  Radiation damage effects

## Slide 2
  Mobile charge creation
  Factors that determine cluster size:
    Track Angle
    Charge carrier diffusion
    Discriminator threshold
    Sensor bias voltage
  Optimal use of charge sharing information

## Slide 3: Mobile charge creation in silicon
One e-hole pair is created per 3.62 eV lost by a particle. On average, 24000 e-hole pairs are created per 300 of track length for a minimum-ionizing particle (~87 KeV lost by track).
We have been using 300 thick sensors so far; nominally expect to use 250 thick sensors in BTeV.
Pulse height distribution is well fit with a Landau function convoluted with a Gaussian.
  Fluctuations are large: FHWM(300 Si)  10000 e-.
  Distribution is asymmetric (long high-energy tail).

## Slide 4
Data from 1999 testbeam run
ADC saturation
Charge loss at
one pixel boundary

## Slide 5: Charge creation & collection
Most e-hole pairs are created within ~3 of track.
  Exceptions are due to “-rays” – electrons with energy of many 10’s of KeV (up to MeV) – these are the cause of the long high energy tail in dE/dx.
  -rays are produced nearly perpendicular to track (elastic scattering kinematics).
Diffusion adds to “width” of track.
  Depends on discriminator threshold and bias voltage.
  Less diffusion at higher bias voltage.
  Effective “width” of track  10
(Simulation)

## Slide 6
Bias Voltage
Discriminator Threshold
Dependence of Cluster Fraction on Bias Voltage and Discriminator Threshold
CAN get 50% charge sharing at normal incidence (50 wide pixels) with sensor just depleted.

## Slide 7: Dependence of cluster size on track angle
1
2
2
3
4
n-side
p-side
50
300
Arctan(1/6) = 9.5°

## Slide 8
Dependence of cluster size on track angle (data from 1999 testbeam run)

## Slide 9
3.3% have more than 2 pixels on.
-rays

## Slide 10: Use of pulse height information
Without knowledge of track angle, the best estimate of track position is given by the digital center of cluster (ignoring pulse height)  x0.
Once the track angle is known, the best estimate of track position is given by x0 + f(,N,PHL,PHR).
For each angle , there are 2-3 possible values of N (others arise from -rays).
PHL,PHR are the pulse heights on the left and right edges of the cluster.
The pulse heights in the center of the cluster contain NO INFORMATION.
  Knowing the track angle means knowing the track length in the central pixels!
The function f is determined from data & simulation.

## Slide 11
Determination of f(,N,PHL,PHR)
Example from 1999 test beam ( = 0°)
Eta = (PHL-PHR)/(PHL+PHR) … really would create a lookup table;
3 bits of pulse height  only 64 possibilities.

## Slide 12
Residual distributions for tracks at normal incidence
xpredicted – x0

## Slide 13
Resolution as a function of track angle
G = standard deviation of Gaussian fit.

## Slide 14: Comments on pulse height measurement
When more than one pixel is hit, either
  Most of the information is in the small pulse height.
  No pulse height is more than ~1/2 MIP.
No need for fine binning of pulse height (fluctuations in dE/dx are large).
1+2  We use only 3 bits for pulse height.
Dynamic range still not finally decided.
  Probably >1/2 MIP, but <1 MIP.

## Slide 15
Small pulse height measurements on cluster edges have large information content --- Low discriminator threshold is important!