## Slide 1
Module 3
DECONTAMINATION
Notes: Instructor Notes
This module contains a lot of procedural information. Emphasize the importance of following procedures and adhering to safety regulations. For some, it may have become routine and they may not recognize the consequences of poor performance. Decontamination is the “messy job” but it is critical to the sterilization and disinfection processes.
Learning activities:
Poll the class asking “What is the most important thing to remember in Decontamination?” Use their answers as a discussion starter to emphasize personal protective equipment, safe conveyance, following procedures, etc.
There is no right answer, because everything is important…this is a way to gauge the knowledge and experience level of your audience.
Points for Discussion
Use the following questions to guide classroom discussion during the presentation of the module.
What is decontamination?
Why is it necessary? (after all most things are going to be sterilized)
How dangerous is the decontamination job?

## Slide 2
Identify the purpose of decontamination.
Detail infection control procedures that are necessary in the decontamination process.
  Identify Personal Protective Equipment.
  Identify guidelines for safely handling sharps.
  Identify hand-washing requirements.
  Identify procedures for handling spills, soiled laundry, and infectious waste.
Detail collection and transportation requirements.
Identify decontamination equipment, procedures, and precautions.
  Identify equipment.
  Detail equipment purpose.
  Describe equipment operating procedures.
  List precautions/exclusions for each piece of equipment.
Notes: Instructor Notes
Review the instructional objectives
You can translate them into common language (“Today we are going to talk about how to remove soil from medical devices while keeping yourself, the staff, the patients, and the medical center environment safe, and limiting the spread of germs.”)
Explain that these objectives reflect what students will be learning in this module and that there will be a self assessment at the end, based on these objectives.
Mention the online course (**insert URL) and that the objectives are the same.

## Slide 3: The Decontamination Area
Physically separated
Restricted access
Adequate lighting and ventilation
Facilitate the collection and transfer of soiled supplies
Notes: Instructor Notes
Emphasize the importance of keeping the decontamination area separated from the rest of SPD.
Depending upon the local facility, this may raise questions. Be prepared to discuss issues regarding the layout and solutions to local concerns.
Learning activities:
Present this as sort of a checklist. If you are familiar with the local facility, discuss each requirement in terms of how the local facility conforms.
Points for Discussion
Does this facility meet all the requirements?
Are there issues or areas for concern?
What is the proper procedure for addressing those concerns?

## Slide 4: Personal Protective Equipment
In Decontamination Area
During Collection
Head/hair cover
Glasses/Goggles/Face Shield
Decontamination Gloves
Gown
Shoe Cover
Cover Gown
Exam Gloves
Notes: Instructor Notes
Stress that the reason for protective gear is to protect the worker and control the spread of infection.
Acknowledge that some of the gear is uncomfortable and people sometimes feel they don’t have time to put it on or change between assignments, but it is a necessity (better safe than sorry).
Emphasize the responsibility for both the employee and the medical center.
Learning activities:
Have sample PPE on hand and demonstrate the proper method of putting them on and taking them off, you can vary the activity by doing it wrong (shake gloves around while pulling them off, handle the contaminated side with your bare hands, etc.), and asking students to point out errors and the rationale behind them.
Points for Discussion
Use the following questions to guide classroom discussion during the presentation of the module.
Who does PPE protect?
How did Universal Precaution/Standards change things?
If you wear gloves, do you still need to wash your hands?

## Slide 5: Cleaning Agents
Detergents
Disinfectants
Notes: Instructor Notes
The purpose of this section is to help the user become familiar with the characteristics and capabilities of both detergent and disinfectant in order to make wise choices when using them.
Learning activities:
Have sample MSDSs available. Read a description of a common, locally used detergent/disinfectant and ask the class to name it.
Take a tour of the storeroom beforehand and make a list of all available cleaning agents. Have individuals volunteer examples of cleaning agents, listing them on the whiteboard or chart and asking the class to “sort” them into either the disinfectant or detergent category. For the disinfectants ask them to indicate “high”, “medium”, or “low” level. This activity will give you an indication of the class’ familiarity with their local agents. You may want to select a couple of less familiar ones and go into detail about their characteristics and MSDS.
Points for Discussion
Use the following questions to guide classroom discussion during the presentation of the module.
What is each of these used for?
What should you do if you start to use a cleaning agent and it doesn’t look or smell right?
Is it OK to mix detergents and disinfectants together to get things even cleaner?
If you are unfamiliar with a particular product, where can you go for information?
If the medical center changes brands or types of cleaner, what should you do?

## Slide 6
Type | Kills: | Appropriate for: | Examples:
High Level | all bacteria, viruses, and fungi, but not bacterial spores | items that have come into contact with body tissue and fluids disinfecting items that come in contact with mucous membranes (respiratory devices, laryngoscope blades) | chlorine dioxide, hydrogen peroxide, and peracetic acid-based formulation
Medium Level | most pathogenic microorganisms and some viruses, but not bacterial spores | effectively killing organisms such as mycobacterium tuberculosis fungi, hepatitis B virus, medium and small size viruses use on I.V. pumps, feeding pumps, etc. | chlorine compounds, alcohols (70 percent to 90 percent ethanol or isopropyl) and some phenolic and iodophor compounds
Low Level | some types of bacteria generally have little effect on viruses and do not kill spores | use in cleaning environmental surfaces, such as table tops, floors, and walls | chlorine compounds (bleach or Sodium Hypochlorite) alcohols (70 percent to 90 percent ethanol or isopropyl) and Quaternary Ammonium Compounds
Disinfectants
Notes: Instructor Notes
It is important for technicians to be familiar with the disinfection capabilities of the products that they use locally. Discuss specific familiar compounds and which category they fit into.
Learning Activities
If group is small enough and has access, walk through the storeroom and classify the disinfectant products by level. If this is logistically not feasible, bring some products into the classroom and ask learners to classify them and discuss their uses.
Points for Discussion
How do you choose what product to use?
If the High Level products kill more, why not just use them all the time?

## Slide 7: pH
Alkaline
Vs.
Acid
Notes: Instructor Notes
PH is a term that a lot of people have heard of (particularly if they have a pool), but they don’t really understand what it means.
Talk about acidity or alkalinity in relative terms.
The concept of a logarithmic scale may be difficult for some to grasp, so pick out some specific examples and talk about them in terms of their “relative” acidity/alkalinity (“Milk of Magnesia is 100 times more alkaline than seawater”).
For a better understanding of pH, check out:
http://library.thinkquest.org/3659/acidbase/ph.html
http://www.chem.ubc.ca/courseware/pH/index.html
Learning activities:
Discuss the pH of common household substances, if you have access to litmus strips, do a demonstration—squeeze various substances into water and then ask the class to predict their pH (will the strip turn pink or blue).
Points for Discussion
Use the following questions to guide classroom discussion during the presentation of the module.
Why does acidity or alkalinity matter?

## Slide 8: Collection and Transport
Notes: Instructor Notes
Transport varies from medical center to medical center, based on the physical layout and collection facilities. Most audiences will be familiar with at least two of the methods.
Learning activities
Talk about the characteristics and benefits of each type.
Discuss scheduling and frequency.
Points for Discussion
Use the following questions to guide classroom discussion during the presentation of the module.
What are the requirements for collection carts?
In a pinch can I use delivery carts for collection (I mean I’m already on the floor delivering supplies, why can’t I just pick up the stuff if I wrap it really tightly?)
How often does pick-up need to be done for OR? Clinics/ other areas?
Which areas are highest use and require the most frequent pickups?
What should you do if an area is constantly calling asking you to come do a pickup? (schedule them more frequently, place more bins/containers in their area)

## Slide 9: The Decontamination Process
Sort soiled instruments and equipment into groups based on how they will be cleaned
Inspect them for damage/missing parts
Remove visible tissue or bone (gross soil)
Clean the device using a neutral detergent (mechanically or by hand)
Apply the appropriate disinfectant
Allow the item to dry
Notes: Instructor Notes
While the basic decontamination process is the same for all equipment, certain devices will require special handling or additional care. Decontamination is a labor intensive and time consuming job, but critical to proper disinfection and sterilization.
Learning activities
Talk about working efficiently. Discuss collection schedules and ways to sort equipment that will help streamline the decontamination process.
Points for Discussion
Use the following questions to guide classroom discussion during the presentation of the module.
What do you do first when unloading soiled equipment?
What special considerations are necessary for equipment sets or loaner equipment?
Do you have to prewash items that are to be cleaned in the Sonic cleaner?

## Slide 10: Types of Equipment To Be Cleaned
Electrical equipment
Non-electrical equipment
Rubber/plastic supplies
Metalware
Glassware
Surgical power equipment
Surgical instruments
Endoscopic equipment
Other
Notes: Instructor Notes
Learners must be able to recognize the different types of equipment and the requirements for cleaning each of them.
Be sure to emphasize Precautions such as:
To prevent cross contamination, always rinse cloth in disinfectant solution between pieces of equipment.
Splashing is likely during this activity. Eye protection and a mask are required.
Scrubbing must be done under the surface of the solution; eye protection is mandatory.
If an item fills with water during processing, use extreme caution during removal. This represents a burn hazard, and protective gloves are required
Before processing any scope, the technician should consult all manufacturer's instructions. NEVER handle the scope by the shaft because it may cause damage.
Microsurgical and delicate eye instruments should not be processed through a washer/sterilizer because the turbulent action of steam mixed with water may cause damage.
Learning activities
Walk through the list, providing examples of each.
Detail the basic procedure for each type and emphasize any precautions. (reference online course http://63.168.206.231/decontamination/lesson_4/de0402.asp current address – change to VA URL when installed on VA server
Points for Discussion
Emphasize the delicacy and high cost of some instruments. Stress following proper procedure to protect self and equipment.

## Slide 11: Using Cleaning Equipment
Washer/Sterilizer
Washer/Sanitizer
Utensil Washer
Pasteurmatic Washer
Scope Washer
Notes: Instructor Notes
These are all dishwasher like devices that use a combination of water motion and detergent to wash soil from device surfaces.
Learning Activities
Discuss the characteristics and uses of each, distinguishing between them.
Provide examples of equipment and ask the class which device would be most appropriate for cleaning it and their rationale for making that choice.
Points for Discussion
How do you choose which equipment to use? Why is one type better than another?
What do you need to remember when loading equipment into these processors?

## Slide 12: Using Cleaning Equipment
Ultrasonic Cleaner
Cart Washer
Steam Cleaning Device
Tube Dryer
Notes: Instructor Notes
These are devices that were designed for a specific cleaning purpose.
Learning Activities
Discuss the characteristics and uses of each, talking about how and why they work and how to get the best service out of each.
Include a discussion of any precautions or issues students may have with using each of them.
Points for Discussion
What is cavitation? How does it work? What types of things can’t be cleaned in the Ultrasonic? What sorts of things can be cleaned in the cart washer? Is it just for carts?
What precautions are necessary when using the steam gun?

## Slide 13: Infection Control
Follow Universal Precaution/Standards
Hand washing
Sharps safety
Spills
Laundry
Waste
Cleanup
Notes: Instructor Notes
Each of these areas contributes to good infection control. Make sure learners understand that ALL of them are necessary to ensure that the chain of infection is broken.
Learning Activities
Discuss the guidelines, walk through the procedure for each and mention any associated precautions.
If facilities are available, demonstrate hand washing procedure and ask students to observe and write down any problems or areas of concern. When you wash your hands, do several of the following:
Run the water for a long time before and after.
Use your bare hand to turn off the faucet.
Skip using soap.
Dry your hands and throw the towel away, then open the door or touch the handle on the towel dispenser – anything to recontaminate yourself.
Solicit pointers/critique from the class. After discussion, demonstrate again, following correct procedure.
Discuss any concerns with waste disposal or clean up procedures, pointing out technicians and others responsibility in each case.
Points for Discussion
Is soap necessary for hand washing? What are some side effects of constant use? How long is long enough?
Are air dryers or paper towels better? What about chemical or waterless hand cleaners?
What is your responsibility in terms of cleaning up spills?
What are the local soiled laundry procedures?
What about waste disposal?
Who is responsible for cleaning up spills?

## Slide 14: Safety
SPD Desk Guide
Material Safety Data Sheets
PPE
Eye Wash Stations
Notes: Instructor notes
The SPD Policy and Procedures Manual provides safety related guidelines for technicians to follow. It is the technician’s responsibility to know and observe safety rules. Many workers are not familiar with the manual and don’t know where it is stored.
Learning Activities
Point out Manual Location
DO a quick walkthrough of contents
Mention update schedule
Pass around MSDS samples—discuss layout and the types of information contained—help learners become comfortable reading and using them ( you might even hand one to everyone and do a paper scavenger hunt: Who can find this type of information fastest? Chemical name, issue date, cautions, etc.)
Points for Discussion
Technician responsibility
Resources

## Slide 15: SPD Environmental Hazards
Open drawers
Sharps and needles
Carelessly stacked washer/sterilizer baskets
Automatic cart washer doors
Lifting heavy objects
Wet, slippery floors
Automatic loaders/unloaders and doors
Hot items
Improper use of chemicals
Equipment noise
Notes: Instructor Notes
The technician needs to learn to recognize environmental hazards and to apply proper safety procedures to avoid injury.
Learning Activities
Discuss possible hazards and means of avoiding injury. If available, discuss local injury statistics. This is also a good place for “war stories” illustrating the hazards of the job.
Discussion Points
What is the biggest cause of injury in the SPD environment?
What factors contribute to the possibility of injury?

## Slide 16
The purpose of decontamination is to:
    a. Protect workers
    b. Ensure the sterility of surgical devices
    c. Reduce the bioburden on reusable devices
    d. Facilitate cross contamination
Notes: Instructor Notes
The slides are designed to display the question first and then fly in the answer on mouse click. You may want to keep track of students questions that recur in order to reinforce them in the next session.
Learning activities:
You can decide how you want to use the review questions:
Assign them as homework
Break the class into small groups and have them answer together (or to save time give each group a subset of the questions)
Project them and solicit verbal answers from volunteers
Strongly recommend that the learners make notes regarding the correct answers (the questions are tied directly to the learning objectives and therefore to the certification test).
Points for Discussion
Use the questions to review and reinforce module content and correct any misconceptions.

## Slide 17
Match each term to its description.
Used for cleaning environmental surfaces such as walls and floors
Aids removal of soil such as blood, pus, and urine
Appropriate for items that will come in contact with body tissues, fluids, or mucous membranes
A measure of the acidity or alkalinity of a substance
Kills most pathogenic microorganisms and some viruses
Low-level disinfectant
Detergent
High-level disinfectant
pH level
Medium-level disinfectant

## Slide 18
Carts
Solid containers
Automated Transports
Dumbwaiters
Wheels require routine lubrication
Must have a tight fitting lid
Require programming by a technician
Must be designated as either clean or dirty
Match each term to its description.

## Slide 19
PPE consists of gloves and a head covering.
Containers must be made of disposable material.
Is done on an “as-needed” basis.
Must be done in a manner that protects the technician, the environment, and the public.
  Which statements apply to soiled equipment collection?

## Slide 20
PPE consists of gloves and a head covering.
Containers must be made of disposable material.
Is done on an “as-needed” basis.
Procedures must protect the technician, the environment, and the public.
  Which statements apply to soiled equipment collection?

## Slide 21
Which of the following can be processed in a washer/sterilizer?
  Flexible endoscope
  Metalware
  Surgical power equipment
  Glassware

## Slide 22
Which of the following can be processed in a washer/sterilizer?
  Flexible endoscope
  Metalware
  Surgical power equipment
  Glassware

## Slide 23
Order the steps for decontaminating surgical instruments.
    Place on trays or washer racks in open position.
    Remove gross soil.
    Process in ultrasonic cleaner.
    Send to prep room.
3
1
2
4

## Slide 24
  Remove bits or blades.
  Wipe hand piece with water- dampened cloth.
  Remove power source.
  Clean hand piece with cleaning solution.
2
4
1
3
Order the steps for decontaminating surgical instruments.

## Slide 25
  Hand-held device used for cleaning wheelchairs and carts.
Name that equipment!
Steam Cleaner

## Slide 26
  Used to dry rubber or plastic goods following cleaning, this device draws in air, heats it, and circulates it through the cabinet.
Name that equipment!
Tube Dryer

## Slide 27
  Uses hot water at 170 degrees F for 30 minutes to clean plastic and rubber tubing.
Name that equipment!
Pasteurmatic

## Slide 28
  Good for cleaning metalware, surgical instruments, and glassware. Uses steam under pressure.
Name that equipment!
Washer/Sterilizer

## Slide 29
  Uses steam to thermally sanitize items. Considered less effective than the Washer/Sterilizer.
Name that equipment!
Washer/Sanitizer

## Slide 30
  Uses sound waves and a process called cavitation to remove soil particles.
Name that equipment!
Ultrasonic Cleaner

## Slide 31
  Requires an adapter to force cleaning solution through the channels of flexible scopes.
Name that equipment!
Scope Washer

## Slide 32
Which statements are true regarding sharps?
  Disposable sharps should be disposed of at the point of use.
  Sharps are not a concern for SPD because they are disposed of by the user.
  Sharps must be disposed of in special containers.
  Sharps generally are reusable and must be reprocessed with care.