## Slide 1: Creation of Gridded MOS Land Water Mask
Statistical Modeling Branch
Meteorological Development Lab
November 9, 2007

## Slide 2: Current GMOS Land Water Mask
Coarse U.S. shapefile from ESRI media DVD
Manual editing tailored to analysis technique
  coastline was adjusted to match station location
  Grid point location not considered in edits

## Slide 3: Purpose of Regenerating Land Water Mask
Common land water mask for GMOS and verification software
  Poor Gridded MOS verifications in coastal areas when compared to NDFD
GMOS users expressed concern along the east coast
  Barrier islands
  Harbor and Bay sizes not accurate

## Slide 4: Current GMOS Land Water Mask

## Slide 5: AWIPS High Resolution Shapefiles
Marine Zones only consider US territory
Mexico & Cuba not available
Includes all US lakes
Gaps between US and Canada where water exists

## Slide 6: AWIPS High Resolution Shapefiles

## Slide 7: Modified AWIPS High Resolution Shapefiles for GMOS
AWIPS States Shapefile
  Removed Lake Okeechobee due to lack of MOS station guidance in the lake
No Mexico AWIPS shapefile
  Used ESRI Media States file
  Drew polygon to “fill in” holes left due to differing resolution with AWIPS states shapefile
Inland Water
  AWIPS Lakes Shapefile
    Selected Great Lakes, Great Salt Lake, & Lake St. Claire
AWIPS Canadian Province Shapefile
  More coarse than AWIPS states shapefile
  Drew polygon to “fill in” holes left due to differing resolutions
Ocean
  No Ocean Shapefiles existed
  Used a rectangular polygon bigger than the coverage area and erased all of the aforementioned shapefiles, so the remaining area became ocean

## Slide 8: Removing Lake Okeechobee
Take care to delete entire sketch, so no residual evidence of the lake is left.

## Slide 9: Shapefile Edits for Land Water Mask
Polygons were dissolved to eliminate holes and boundaries
Inland water, Ocean, and Land shapefiles were merged to form a single shapefile
  Attribute field indicates land or water
    Ocean = 0
    Inland Water = 3
    Land = 9

## Slide 10: Land Water Mask Shapefile

## Slide 11: Land Water Mask Shapefile
Polygon Shapefile converted to Raster GRID
Raster cell given value of polygon directly under the CENTER of the grid cell
Check was made by assigning polygon value to NDFD points
Grid values were extracted to points

## Slide 12: New Land Water Mask

## Slide 13: New Land Water Mask Areas of Forecaster Concern
KMLB
KBOX
KOKX
KILM
KGYY

## Slide 14: Difference in Current GMOS and New Land Water - KGYY

## Slide 15: Temperature F24 November 4, 2007 12Z Cycle Proposed Land Water Mask
maps are available on web site as *.pdf files with zoom capability

## Slide 16: Temperature F24 November 4, 2007 12Z Cycle Operational Land Water Mask
maps are available on web site as *.pdf files with zoom capability

## Slide 17: Resources and Contact Information
Web Based Land Water Mask Comparison
AWIPS Map Database – shapefile source
ESRI’s ArcInfo 9.2 was used to create the land water mask
For Further information
  Kari Sheets, SMB GIS team lead
    301-713-0023 ext 125
    Kari.sheets@noaa.gov