## Slide 1
Polluted profile from GEOS-Chem model used as initial guess
Doubled emissions to obtain new profile
Ran forward model over new profile to obtain simulated spectrum
  Added noise
Performed retrieval
Satellite Observations of Tropospheric Ammonia - Motivation and First Results
1. Motivation
Nitrogen in ammonia is deposited to Earth’s surface
  Excess nitrogen leads to:
    Nutrient imbalances
    Change in ecosystem composition
    Algal blooms
    Hypoxia
Ammonium sulfate and ammonium nitrate form 10-20% of fine particulate matter (PM2.5) in atmosphere over the US
  Exceeds recommended threshold (WHO, 2003)
  Excessive exposure to aerosol concentration is associated with :
    Increased chances of cardiovascular disease
    Inhibited lung development
    Premature death
    References (Burnett et al., 2000; Dominici et al., 2006; Gauderman et al., 2004; Pope , 2000; Pope et al., 2002)
  Fine particulates are also responsible for reduced visibility in national parks and scenic areas (Malm et al., 2000)
Point sources and short lifetime (less than 10 days) lead to high temporal and spatial variability
In-situ measurement of ammonia are difficult and sparse
    mostly confined to near surface
Physical and chemical processes governing ammonia emissions are challenging to quantify
3. Proof of concept NH3 retrieval from TES
Simple scaling of NH3 profile to reduce residuals (Beer et al., 2008)
CHINA
WEST COAST
 Elevated amounts over Beijing, China, July 10, 2007
 TES spectra can provide information on NH3 variability
2. What TES can provide
TES data have been collected over most of the Earth’ surface since July 2004
TES can provide time series of NH3 mixing ratios almost anywhere on the globe
This dataset will provide a quantitative, global, long-term picture of NH3 spatial and temporal variability
First objective: provide monthly means for a year
  Compare with output from regional (e.g., CMAQ) and global models (e.g., GEOS-Chem)
Future objective:
  Use intensive TES Special Observations to obtain NH3 concentrations over areas of high emission (e.g. North Carolina, Midwest)
Compare with in-situ measurements:
   More realistic spatial and temporal distribution of ammonia emissions
   Example: determine whether peak of NH3 emissions is:
    In the spring (correlated with fertilizer application)
    In the summer (higher temperatures lead to higher NH3 emissions from manure piles)
5. Sample retrieval: Doubling of NH3 emission
Retrieved-truth differences are within error bars
Retrieved profile is significantly different from a priori
  TES retrieval provided added information
Mark W.Shephard, Karen E. Cady-Pereira, Vivienne H.Payne AER, Inc. | Ming Luo, Curtis P. Rinsland, Reinhard Beer, Greg Osterman, Kevin Bowman NASA-JPL | Daven Henze Columbia University | Robert W.Pinder US EPA-ORD | Gary Lear US EPA-CAMD | Shephard A. Clough Clough Associates
Spectrum from TES pass over Beijing
4. Retrieval Procedure
Optimal estimation approach. (Rodgers, 2000)
  ill-posed problem (number of potential solutions)
  nonlinear least square with constraints
a priori estimate
  GEOS-Chem profiles binned by surface NH3 amount
6. Datasets for the Evaluation of TES NH3 Retrievals
GEOS-Chem Output for 2005
EPA NH3 Monitoring Network
Sampling began at most sites in October 2007
a priori for TES scans over China
Latitude (deg)