## Slide 1: Response Regarding Detector Optimization
Kevin McFarland University of Rochester MINERvA Director’s Review 10-11 January 2005

## Slide 2: Basic Detector Geometry


Coil
Active segmented scint. detector 5.87 tons
~1 ton of US nuclear target planes (C, Fe, Pb)
DS Cals, Nucl. Targets just add absorber to scintillator planes
Magnetized OD (HCAL) frames
Notes: Cartoon of the detector: walk through from inside
emphasize: active and upstream targets, magnetized OD

## Slide 3: Vital Statistics of MINERvA
Number of Channels | 30992
Channels in ID+CALS | 25088
Channels in OD | 5904
Volume of Scintillator (m3) | 22.5
WLS Fiber (km) | 90.7
Clear Fiber (km) | 41.6
Number of M-64 PMTs | 503
Mass of ID (metric tons) | 10.8
Mass of OD in ID region (metric tons) | 98.0
Mass of CALS, Nuclear Targets (metric tons) | 27.2
Mass of OD in CAL region (metric tons) | 62.9
Total MINERvA Mass (metric tons) | 199
Plastic Region Mass (metric tons) | 5.87
Data Rate (bits/spill) | 7.9E+6
Notes: channels: dominated by ID and nuclear targets (~20% from calorimeters, ~20% from OD)
mass dominated by OD

## Slide 4: Cost Summaries

## Slide 5: What Does it Take to Reduce Costs in Channels and Modules?
Number of channels…
  roughly, I guestimate the marginal channel cost to be $110
  largest items: ~$20 for electronics, ~$35 for PMT and testing, $30 for PMT box, ~$15 for fiber
    so saving $1M takes approximately 9K channels (of 31K)
  Note… there are granularity issues that make this tough to realize
More gains by reducing number of modules
  win on channels, module and plane production
  there are 49 modules in current design, 30 fully active, 9 nuclear targets, 10 downstream calorimeters, each with roughly 2% of the channels
  I guestimate marginal cost of a module to be 0.11M$, about $0.7M of which is in the channel count; so that means 9 modules away to save $1M
Please take this with very large grains of salt; it is based on quick fudges to a costing model we had when optimizing

## Slide 6: Constraints on Extrusions
MINOS experience: 1x4cm extrusions are near limit of surface are to volume ratio for successful extrusion
  so the largest granularity we might consider is 5x2.5cm triangles, just on technical grounds? we certainly never considered anything beyond this
  for comparison, 3cm^2 MINERvA cross-section is same as SciBar at K2K
Then, we looked at our key design parameters
  z resolution: width and thickness both contribute
  efficiency for quasi-elastics: primarily thickness of extrusions
  in the end, we took a hit on the latter in exchange for preserving the former
Final fiducial volume: want roughly a cube
  based on acceptance studies, particles go at wide angles
  3 ton fiducial volume target.

## Slide 7: Optimization of Tracking in Active Target
technique pioneered by D0 upgrade pre-shower detector
Excellent tracking resolution w/ triangular extrusion
  ~3 mm in transverse direction from light sharing
  More effective than rectangles (resolution/segmentation)
  Key resolution parameters:
    transverse segmentation and light yield
    longitudinal segmentation for z vertex determination
3.3cm
Coordinate residual for different strip widths
4cm width
3cm width (blue and green are different thicknesses)
Notes: Intro: optimizing detector: granularity and the other is OD size
light sharing gets us good resolution
optimization: pick width well matched with multiple-scattering limitations, light yield limitations (photostatistics)
segmentation in z set by need for efficiency with short tracks

## Slide 8: CCQE Vertex Efficiency vs. Absorber
CCQE
Here what is being studied is the resolution (and efficiency) of reconstructing CCQE vertex
Green is 1.0cm z sampling Blue is 1.5cm z sampling Read is 2.0cm z sampling (we opted for 1.7cm)
Obviously, this one hurts…
Big effect is inability to pick up short proton tracks
For nuclear targets, require resolution < 1cm

## Slide 9: Size of the Outer Detector
Outer Detector (OD) steel is a cost-driver (and mass-driver) for the experiment
  optimized for: containment of hadronic energy in DIS events and tracking of sideways going muons (B-field)
  “step” in detector is result of shaving upstream end thickness
Notes: outer detector: need to contain most particles in events, or else lose high multiplicity events (DIS) with energy leakage
but OD width is a cost driver
two compromises: step granularity (5cm->10cm); and step in z since most US part is not populated (backwards particles soft)

## Slide 10: Size of OD (cont’d)
How chosen?
Hadronic energy resolution of approximately 20-30%/sqrt(E) for DIS
This is the average leakage
  RMS fluctuations are five times larger than average leakage due to tail (could not dig up this plot; sorry)
  So goal was to keep leakage contribution to this to <10%
  Rationale was that this resolution effect would be hard to understand
Ergo… 50 cm
  later thinned upstream part to 30cm
Energy Containment in Nuclear Target Region vs. Outer Detector Thickness
thickest part of OD

## Slide 11: Example Events
Quasi-elastic n–p
  proton and muon tracks are clearly resolved
  observed energy deposit is shown as size of hit; can clearly see larger proton dE/dx
  precise determination of vertex and measurement of Q2 from tracking

p

nuclear targets
active detector
ECAL
HCAL

## Slide 12: Example Events (cont’d)
0 Production
  two photons clearly resolved (tracked). can find vertex.
  some photons shower in ID, some in side ECAL (Pb absorber) region
  photon energy resolution is ~6%/sqrt(E) (average)



nuclear targets
active detector
ECAL
HCAL
Notes: note ability to track photons… resolve vertex and look for activity (find it here)