## Slide 1: MINERvA Detector “Optimization”
Kevin McFarland University of Rochester 26 February 2005 MINERvA Collaboration meeting

## Slide 2: Optimization?
We were beaten up at our Temple review for not being able to show sufficient evidence of physics vs. $ optimization
  my opinion: probably more than we deserved
  but it is still a valid point
  we want such information to understand what happens if we get on 80% of our proposed funds, for example, or to see if we can build more slowly than we propose and do physics during construction

## Slide 3: In which direction?
Dave C. pointed out that “optimization” also means we should think of add-ons
  if we have project funds left, what could we do at the end to improve the experiment? DS HCAL magnetization, for example
But the sense in which the committee wanted us to study was clearly de-scoping, not up-scoping…

## Slide 4: Tools
We need to do some more Monte Carlo simulation studies with different geometries
We need better tools for evaluating the impact of changes on costs
Here is what was presented to the Temple review

## Slide 5: What Does it Take to Reduce Costs in Channels and Modules?
Number of channels…
  roughly, I guestimate the marginal channel cost to be $110
  largest items: ~$20 for electronics, ~$35 for PMT and testing, $30 for PMT box, ~$15 for fiber
    so saving $1M takes approximately 9K channels (of 31K)
  Note… there are granularity issues that make this tough to realize
More gains by reducing number of modules
  win on channels, module and plane production
  there are 49 modules in current design, 30 fully active, 9 nuclear targets, 10 downstream calorimeters, each with roughly 2% of the channels
  I guestimate marginal cost of a module to be 0.11M$, about $0.7M of which is in the channel count; so that means 9 modules away to save $1M
Please take this with very large grains of salt; it is based on quick fudges to a costing model we had when optimizing

## Slide 6: Constraints on Extrusions
MINOS experience: 1x4cm extrusions are near limit of surface are to volume ratio for successful extrusion
  so the largest granularity we might consider is 5x2.5cm triangles, just on technical grounds? we certainly never considered anything beyond this
  for comparison, 3cm^2 MINERvA cross-section is same as SciBar at K2K
Then, we looked at our key design parameters
  z resolution: width and thickness both contribute
  efficiency for quasi-elastics: primarily thickness of extrusions
  in the end, we took a hit on the latter in exchange for preserving the former
Final fiducial volume: want roughly a cube
  based on acceptance studies, particles go at wide angles
  3 ton fiducial volume target.

## Slide 7: Optimization of Tracking in Active Target
technique pioneered by D0 upgrade pre-shower detector
Excellent tracking resolution w/ triangular extrusion
  ~3 mm in transverse direction from light sharing
  More effective than rectangles (resolution/segmentation)
  Key resolution parameters:
    transverse segmentation and light yield
    longitudinal segmentation for z vertex determination
3.3cm
Coordinate residual for different strip widths
4cm width
3cm width (blue and green are different thicknesses)
Notes: Intro: optimizing detector: granularity and the other is OD size
light sharing gets us good resolution
optimization: pick width well matched with multiple-scattering limitations, light yield limitations (photostatistics)
segmentation in z set by need for efficiency with short tracks

## Slide 8: CCQE Vertex Efficiency vs. Absorber
CCQE
Here what is being studied is the resolution (and efficiency) of reconstructing CCQE vertex
Green is 1.0cm z sampling Blue is 1.5cm z sampling Read is 2.0cm z sampling (we opted for 1.7cm)
Obviously, this one hurts…
Big effect is inability to pick up short proton tracks
For nuclear targets, require resolution < 1cm

## Slide 9: Size of the Outer Detector
Outer Detector (OD) steel is a cost-driver (and mass-driver) for the experiment
  optimized for: containment of hadronic energy in DIS events and tracking of sideways going muons (B-field)
  “step” in detector is result of shaving upstream end thickness
Notes: outer detector: need to contain most particles in events, or else lose high multiplicity events (DIS) with energy leakage
but OD width is a cost driver
two compromises: step granularity (5cm->10cm); and step in z since most US part is not populated (backwards particles soft)

## Slide 10: Size of OD (cont’d)
How chosen?
Hadronic energy resolution of approximately 20-30%/sqrt(E) for DIS
This is the average leakage
  RMS fluctuations are five times larger than average leakage due to tail (could not dig up this plot; sorry)
  So goal was to keep leakage contribution to this to <10%
  Rationale was that this resolution effect would be hard to understand
Ergo… 50 cm
  later thinned upstream part to 30cm
Energy Containment in Nuclear Target Region vs. Outer Detector Thickness
thickest part of OD

## Slide 11: What’s Next?
I compiled a list of ID granularity and OD size optimization studies to pursue
  input from Steve B. and Dave C.
  these are “de-scoping” studies

## Slide 12: OD optimization
Start with an OD like ours but with 30cm extra material everywhere.
For a hypothetical OD with 10cm, 20cm, 30cm extra and 10cm, 20cm less, plot:
  muons escaping for QE Q2>3 GeV^2 in ID and in nuclear targets. Do this only for "trackable" muons (6 or 9 planes of scint.)
  fraction of DIS energy contained (high x and low x?, ID and nuclear targets separated?)
  RMS fractional DIS energy leaked (high x and low x? ID and nuclear targets separated?)
I think we more or less have first one in hand. We've done things similar to the others; it's not hard.

## Slide 13: z segmentation of ID
Dave C. showed this well at the Aug '03 JLab meeting, but we could repeat the study?
He looked at efficiency for QE (low Q^2) reconstruction vs. z spacing.
  Could use 1.7cm, 2.2 cm, 2.7cm, 1.2cm, 0.7cm...
  Want to show both efficiency and z vertex resolution.

## Slide 14: Strip width optimization
This one is much more tricky.
I think something like 2.8, 3.3, 3.8, 4.3, 4.8 is a good range of cells to try. So...
  sigma z_vertex for two track QE events
  efficiency for two track QE events (are tracks separated with such big cells)
  for coherent CC events, Hugh's t variable which plays a big role in his cuts
  for DIS events, how close to the vertex can the track be tracked? I'm not sure we have a way to translate that into an effective z vertex resolution? maybe look at events with multiple tracks?
  I'd like to figure out how it affects photon ID (since I think track width is likely to be a key parameter) but we don't really have the tools

## Slide 15: We also should catalog
Effects of different numbers of modules (or module width) on fiducial events for different flag ship analyses
  QEs, single pi0 resonant, coherent CC/NC, DIS