## Slide 1: Plans for a Speciated Ambient Mercury Monitoring Network
Presented at the
2006 National Air Quality Conference
Presented by
Kevin A. Cavender
EPA/OAQPS
October 6, 2005

## Slide 2: Overview
Why monitor mercury?
Current mercury monitoring
Why do we need speciated data?
Technologies
Network strategy
Questions and answers

## Slide 3: Why Monitor Mercury?
Mercury is a persistent bioaccumulative toxic (PBT)
Impairs neurological development in babies and young children
Main pathway is fish consumption

## Slide 4: Mean Mercury Concentrations for Top 24 Types of Fish Consumed in U.S. Commercial Seafood Market
Source: Carrington and Bolger, 2002

## Slide 5: CAIR and CAMR Accountability
The Clean Air Interstate Rule and the Clean Air Mercury Rule (CAIR, CAMR) will reduce mercury emissions from coal-fired power plants.
Under several mandates such as the Government Performance and Results Act (GPRA), and the Program Assessment Rating Tool (PART), the EPA will be expected to assess reductions in deposition and risk due to these rules.
Tracking progress and results is a critical step in improving air quality management programs (National Research Council, “Air Quality Management in the United States”, 2004).
Determine if additional emission reductions are needed to protect human health and ecosystem welfare.
Show we know what we are doing

## Slide 6: CMAQ Estimated 2001 Total Mercury Deposition

## Slide 7: CMAQ Estimated Reduction in Total Mercury Deposition Due to CAIR/CAMR (2020)

## Slide 8: Improve Mercury Modeling
Current transport and deposition model estimates are very uncertain due to lack of data to validate models
Data on speciated ambient mercury needed to validate these models.

## Slide 9: Mercury Deposition Network
  Started in 1995
  Wet deposition in rain and snow
  Unspeciated
  No dry deposition (no data to estimate it)
  Broad geographic coverage (including Canada and Mexico), though fewer sites in cities and west of the Mississippi River
  Part of NADP, individual sites sponsored by Federal, State, and local organizations
  http://nadp.sws.uiuc.edu/mdn/

## Slide 11: Total Mercury Wet Deposition, 2003

## Slide 12: Current Gaps in Mercury Monitoring
No dry deposition monitoring (or surrogate)
Current direct dry deposition methods not practical for routine network
MDN coverage poor in western states
Current MDN not adequate for tracking impact of CAMR

## Slide 13: Recommendations for Improving Mercury Monitoring
Develop method to routinely measure or estimate dry deposition
  Current dry deposition methods are too expensive/intensive for routine use
  ORD working on improving methods to allow for limited deployment for model development
  Deploy network of currently available continuous total/speciated ambient air mercury monitors as surrogate
  Models to be developed that relate these speciated air measurements to dry deposition

## Slide 14: Why do We Need Speciated Data?
Direct dry deposition measurements are not practical at this time.
Speciated mercury data needed to estimate dry deposition
Dry deposition can be from 0.25 to 3 times wet deposition, depending on location
~98% of total ambient mercury is elemental mercury, yet deposition rates are driven by particulate and oxidized Hg

## Slide 15: Speciated Ambient Mercury Methods
Continuous monitors
  Tekran
  Others?
Manual Method

## Slide 16: Tekran Continuous Speciated Ambient Mercury Monitor
Provides semi-continuous measurements of Hgo, Hg(II), and Particulate Hg
Fairly high capital cost
Lower operating costs
Lots of data – 1 sample/3hours

## Slide 17: Manual Method
Same principle as continuous, but analysis occurs back in the lab
Provides integrated measurements of Hgo, Hg(II), and Particulate Hg
Low capital cost
Higher operating costs
Lower data resolution (1 in 3 days, 1 in 6 days, etc.)

## Slide 18: Looking Beyond Current Methods
Looking for other vendors to enter the market
Push for new or improved methods that –
  Reduce costs
  Improve performance
  Less intensive

## Slide 19: Network Strategy
Work with NADP to expand MDN to include speciated ambient mercury monitoring
Build infrastructure and support for network operations
Partner with other Federal, state, and local agencies to “sponsor” sites
Mix of continuous and manual sites
“Build it and they will come” approach

## Slide 20: Questions